## Slide 1: Class I Organic Solvents
Chloroform CHCl3 CAS RN:67-66-3、865-49-6 |  |  | 
Health Hazards | Possible diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Airway irritation, Hepatic impairment, Renal impairment, Cardiovascular disturbances, Suspected carcinogenicity, Suspected reproductive toxicity. | 
 | Symptoms | Eye pain, tearing, conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, heaviness, Dizziness, Unsteadiness, Drowsiness, Nausea, Vomiting, Loss of appetite, Sensory abnormalities, General fatigue, Cough, Shortness of breath, Nasal discharge, Nasal congestion, Sore nose/throat, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Swelling, Weight loss | 
Handling Precautions | ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in a well‑ventilated area. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※Select glove materials appropriate for the chemical and replace gloves after permeation time (or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage
 | Type of respiratory protection |  | Organic vapor respirator (Select specific type based on work conditions or consult the equipment manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・Special treatment may be required. ・Seek medical attention if feeling unwell. | 
 | If on skin | ・Wash with plenty of water and soap. ・Seek medical advice if irritation occurs. ・Remove contaminated clothing and wash before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do. Continue rinsing. ・Seek immediate medical advice. | 
 | If swallowed | ・Seek medical attention if feeling unwell. ・Rinse mouth. | 

## Slide 2: Class I Organic Solvents
Carbon tetrachloride CCl4 CAS RN:56-23-5 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, CNS impairment, Hepatic injury, Renal dysfunction, Gastrointestinal disorders, Carcinogenicity, Reproductive toxicity. | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Redness, Eczema, Urticaria, Headache, Dizziness, Drowsiness, Nausea, Vomiting, Fatigue, Jaundice, Urination abnormalities(polyuria/oliguria), Swelling, Abdominal pain, Diarrhea, Appetite loss, Facial pallor, Palpitations, Weight loss | 
Handling Precautions | ・Use only outdoors or in well‑ventilated areas. ・Avoid inhalation of dust or vapor. ・No eating, drinking, or smoking in use areas. ・Keep containers tightly closed. ・Avoid environmental release. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※Select glove materials appropriate for the chemical and replace gloves after permeation time (or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage
 | Type of respiratory protection |  | Organic vapor respirator (Select specific type based on work conditions or consult the equipment manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and keep them at rest in a position comfortable for breathing. •Seek medical attention if feeling unwell. | 
 | If on skin | ・Wash with plenty of water and soap. ・Seek medical advice if irritation occurs. ・Remove contaminated clothing and wash before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do. Continue rinsing. ・Seek immediate medical advice. | 
 | If swallowed | ・Rinse mouth. ・Seek medical attention if feeling unwell. | 

## Slide 3: Class I Organic Solvents
1,2-Dichloroethane ClCH₂–CH₂Cl CAS RN:107-06-2 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system impairment, Peripheral neuropathy, Airway irritation, Pulmonary impairment, Liver damage, Kidney damage, Cardiovascular disturbances, Hematologic disorders, Gastrointestinal impairment, Endocrine disruption(thyroid), Carcinogenicity. | 
 | Symptoms | Eye pain, tearing, Conjunctival redness, Skin inflammation, Pruritus(Itching), Skin redness, Headache, Heaviness, Dizziness, Drowsiness, Nausea, Vomiting, General fatigue Cough, Shortness of breath, Nasal discharge, Nasal congestion, Nose or throat pain, Palpitations, Diaphoresis, Chest pain, Breathing difficulties, Easy fatigability, Jaundice, Hematuria, Increased urination, Decreased urination, swelling, Abdominal pain, Diarrhea, Loss of appetite, Pallor, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flames, or hot surfaces. ・Keep containers tightly closed. ・Take precautions against static discharge. ・Do not inhale dust, fumes, or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in a well‑ventilated area. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select gloves appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × ◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high concentrations of vapors, such as leakage zones or third‑control‑area environments.
 | Type of respiratory protection |  | Organic vapor respirator(Select based on working conditions or consult manufacturer.)
First Aid Measures | If inhaled | ・Seek medical evaluation if feeling unwell. ・Seek medical attention if symptoms persist. | 
 | If on skin | ・Rinse thoroughly with plenty of water. ・Seek medical attention if symptoms persist. | 
 | If in eyes | ・Rinse cautiously with water for 15–20 minutes. Remove contact lenses if easy to do so; continue rinsing. ・Seek medical advice if symptoms persist. | 
 | If swallowed | ・Rinse mouth with water. ・Seek immediate medical attention. | 

## Slide 4: Class I Organic Solvents
1,1,2,2-Tetrachloroethane Cl₂CH–CHCl₂ CAS RN:79-34-5 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system effects, Airway irritation, Liver damage, Kidney damage, Carcinogenicity. | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Skin inflammation, Pruritus(Itching), skin redness, Cough, Sputum, Shortness of breath, Nose and throat pain. Headache, Heaviness, Dizziness, Drowsiness, Nausea, Vomiting, General fatigue, Easy fatigability, Facial pallor, Palpitations, Jaundice, Hematuria, Increased urination, Decreased urination, Swelling, Weight loss | 
Handling Precautions | ・Do not inhale dust, fumes, or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in a well‑ventilated place. ・Keep containers tightly closed. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※Select glove materials appropriate for the chemical. Replace gloves once permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentrations such as leakage zones or third‑control‑area levels.
 | Type of respiratory protection |  | Organic vapor respirator(Select appropriate type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and keep them at rest in a position comfortable for breathing. ・If exposure is suspected: seek medical advice. ・Seek medical attention if feeling unwell ・Special treatment may be required. | 
 | If on skin | ・Wash thoroughly with plenty of water and soap. ・Special treatment may be required. ・Seek medical advice if irritation occurs. ・Remove contaminated clothing and wash before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do so; continue rinsing. ・Seek medical attention if irritation persists. | 
 | If swallowed | ・Rinse mouth. ・Seek medical attention if feeling unwell. | 

## Slide 5: Class I Organic Solvents
Trichloroethylene ClCH=CCl₂ CAS RN:79-01-6 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system impairment, Peripheral nerve disorders(including optic nerve and trigeminal nerve impairment), Airway irritation, Pulmonary impairment, Liver damage, Kidney damage, Kidney cancer, Liver and biliary tract cancer, Hematologic malignancies, and suspected reproductive toxicity. | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Eczema, Urticaria, Headache, Heaviness, Dizziness, Drowsiness, Nausea, Vomiting, General fatigue, Tremors, Sensory abnormalities in the limbs, Movement disorders of the extremities, Cough, Sputum, Shortness of breath, Nose and throat pain, Chest pain, Breathing difficulty, Facial pallor, Palpitations, Easy fatigability, Jaundice, Hematuria, Increased urination, Decreased urination, Swelling, Enlargement of cervical or other lymph nodes, Weight loss | 
Handling Precautions | ・Do not inhale dust, fumes, or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in well‑ventilated environments. ・Do not allow contaminated work clothing to leave the workplace.。 ・Keep containers tightly closed. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile: No data, Latex: No data, Chloroprene: No data, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and keep them at rest in a comfortable position. A semi‑sitting posture is recommended. ・Artificial respiration may be required; contact medical services immediately. | 
 | If on skin | ・Wash with plenty of water and soap. ・If skin irritation or rash occurs: seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do; continue rinsing. ・Seek medical attention if irritation persists. | 
 | If swallowed | Rinse mouth. Do not induce vomiting. Contact medical care immediately. | 

## Slide 6: Class I Organic Solvents
1,2-Dichloroethylene CHCl=CHCl CAS RN:540-59-0、156-59-2、156-60-5 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Skin itching, Skin redness, Headache, Heaviness in the head, Dizziness, Drowsiness, Vomiting, General fatigue. | 
Handling Precautions | ・Keep away from heat, sparks, open flames, and other ignition sources ・Keep container tightly closed. ・Ground/bond container and receiving equipment. ・Use non‑sparking tools. ・Take precautionary measures against static discharge. ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in a well‑ventilated place. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and allow rest in a position comfortable for breathing. ・Seek medical attention if symptoms persist. | 
 | If on skin | ・Wash skin immediately. ・Wash thoroughly with plenty of water and soap. ・Seek medical advice if irritation occurs. ・Remove contaminated clothing and wash before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easily possible and continue rinsing. ・Seek medical attention immediately. | 
 | If swallowed | ・Rinse mouth. ・Seek medical attention if feeling unwell. | 

## Slide 7: Class I Organic Solvents
Carbon disulfide CS2 CAS RN:75-15-0 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, airway disorders, Central nervous system disorders, Peripheral nervous system disorders, mental disorders(e.g., delirium, manic–depressive symptoms), Kidney disorders, Vascular abnormalities(e.g., arteriosclerosis), Possible reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Delirium or mood disturbances, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory abnormalities in the limbs, Motor impairment in the limbs, Visual impairment, Cough, Shortness of breath, Runny nose, Nasal congestion, Nose/throat pain, Hematuria, Increased or decreased urination, Edema | 
Handling Precautions | ・Keep away from heat, sparks, open flames, and hot surfaces. ・Keep container tightly closed ・Take measures to prevent static discharge. ・Avoid inhalation of dust or vapor. ・Pregnant or nursing individuals should avoid exposure. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in well‑ventilated areas. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | Move the person to fresh air. Allow them to rest in a position comfortable for breathing. Contact medical services. | 
 | If on skin | ・Immediately remove all contaminated clothing. Wash skin thoroughly with running water or shower. ・Seek medical attention if irritation occurs. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easily possible. Continue rinsing ・Seek medical attention if irritation persists. | 
 | If swallowed | Do not give anything by mouth. Contact medical services immediately. | 

## Slide 8: Class II Organic Solvents
Ethylbenzene C₆H₅–CH₂CH₃ CAS RN:100-41-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Peripheral neuropathy, Hearing impairment, Respiratory tract disorders, Liver disorders, Kidney disorders, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival injection, Skin redness, Headache, Heavy head sensation, Dizziness, Drowsiness, Vomiting, General fatigue, Haring loss, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Facial pallor, Palpitations, Unsteadiness, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Weight loss | 
Handling Precautions | ・Keep away from heat, hot surfaces, sparks, open flame or other ignition sources. ・Keep containers tightly closed. ・Take measures to prevent static‐electric discharge. ・Do not inhale dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated areas. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air; have them rest in a position comfortable for breathing. ・If exposure is known or suspected, seek medical attention. ・Seek medical attention if feeling unwell. | 
 | If on skin | If on skin or hair, remove all contaminated clothing immediately. Rinse affected area with water or take a shower. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do; continue rinsing. ・If eye irritation persists, obtain medical attention. | 
 | If swallowed | ・Contact a physician immediately. ・Do not induce vomiting. | 

## Slide 9: Class II Organic Solvents
1,4-Dioxane O–(CH₂–CH₂)₂–O CAS RN:123-91-1 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders, Pulmonary disorders, Liver disorders, Kidney disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Heavy-headedness, Dizziness, Seizures, Drowsiness, Nausea, Vomiting, General fatigue, Facial pallor, Palpitations, Cough, Shortness of breath, Rhinorrhea, Nasal congestion, Throat pain, Chest pain, Difficulty breathing, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Weight loss | 
Handling Precautions | ・Keep away from heat, hot surfaces, sparks, open flame and other ignition sources. ・Keep containers tightly closed. ・Take measures to prevent static‐electric discharge. ・Use only outdoors or in well-ventilated areas. ・Wash hands thoroughly after handling. ・Do not inhale dust or vapor. ・Do not eat, drink or smoke in the work area. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move victim to fresh air and keep at rest in a position comfortable for breathing. • If unresponsive but breathing, place in the recovery (side-lying) position and protect against hypothermia. • If breathing is difficult, administer oxygen. • If airway irritation or bronchospasm develops, inhaled glucocorticoid spray may be used. • Seek medical examination and treatment if symptoms occur. | 
 | If on skin | ・Immediately remove all contaminated clothing. • Rinse affected skin under running water or shower for at least 10–20 minutes. • Seek medical attention if irritation or rash develops. | 
 | If in eyes | Hold eyelids open and flush with low-pressure water for at least 10 minutes. | 
 | If swallowed | ・If conscious, give 1–2 cups of water to drink. • If vomiting occurs, prevent aspiration by keeping the head lower than the chest in a prone position. | 

## Slide 10: Class II Organic Solvents
Dichloromethane CH2Cl2 CAS RN:75-09-2、1665-00-5 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Airway disorders, Lung disorders, Liver disorders, Bile duct cancer, Male reproductive disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Reduced concentration, Nausea, Vomiting, General fatigue, Facial pallor, Palpitations, Chest pain, Shortness of breath, Weight loss | 
Handling Precautions | ・Do not inhale dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in well‑ventilated areas. ・Keep container tightly closed. ・Avoid release into the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile: No data, Latex: No data, Chloroprene: No data, Neoprene: No data (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and allow rest in a position comfortable for breathing. ・Seek medical attention if feeling unwell. | 
 | If on skin | ・Wash thoroughly with plenty of water and soap. ・If irritation occurs, seek medical attention. | 
 | If in eyes | ・Rinse with water for several minutes. Remove contact lenses if easy. Continue rinsing. ・Seek medical attention if irritation persists. | 
 | If swallowed | ・Rinse mouth ・Seek medical attention if feeling unwell. | 

## Slide 11: Class II Organic Solvents
1,2-Dichloropropane CH₃–CHCl–CH₂Cl CAS RN:78-87-5 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Airway disorders, Lung disorders, Liver disorders, Bile duct cancer, Male reproductive organ disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Reduced concentration, Nausea, Vomiting, General fatigue, Easily fatigued feeling, Jaundice, Facial pallor, Palpitations, Chest pain, Difficulty breathing, Shortness of breath, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flames, and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static discharge. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in well-ventilated areas. ・Keep contaminated work clothes inside the workplace. ・Avoid inhaling dust or vapor. ・Avoid release into the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move person to fresh air. ・If breathing is difficult, administer oxygen. ・If breathing stops, perform mouth-to-nose resuscitation or, if not possible, mouth-to-mouth. ・If cardiac arrest occurs, perform chest compressions and use AED if available. Seek medical attention. | 
 | If on skin | ・Remove contaminated clothing. ・Wash skin thoroughly with water and soap. ・Seek medical attention. | 
 | If in eyes | Rinse eyes with plenty of running water for at least 10 minutes. Remove contact lenses if easy. Continue rinsing. Seek medical attention. | 
 | If swallowed | Rinse mouth. Do not induce vomiting. Do not administer oils, milk, or alcohol. Seek immediate medical attention. | 

## Slide 12: Class II Organic Solvents
Styrene C₆H₅–CH=CH₂ CAS RN:100-42-5 |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Anterior eye disorders, Central nervous system disorders, Peripheral nervous system disorders, Visual impairment, Hearing impairment, Liver disorders, Airway disorders, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory abnormalities in limbs, Motor impairment in limbs, Vision loss or visual impairment, Hearing loss, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Facial pallor, Palpitations, Easy fatigability, Swelling of lymph nodes (e.g., neck), Jaundice, Weight loss | 
Handling Precautions | ・Keep away from heat, hot surfaces, sparks, open flames, and other ignition sources. ・Keep container tightly closed. ・Store in a cool place. ・Take measures to prevent static discharge. ・Do not inhale dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in well‑ventilated areas. ・Avoid release into the environment |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and allow rest in a position comfortable for breathing. ・Seek medical attention. | 
 | If on skin | ・Wash with plenty of water and soap. ・Immediately remove all contaminated clothing. Wash skin with water or shower. ・Seek medical attention if irritation occurs | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy. Continue rinsing. ・Seek medical attention if irritation persists. | 
 | If swallowed | ・Contact a physician immediately. ・Do not induce vomiting. Rinse mouth and give 1–2 cups of water to drink. ・Keep the person at rest. | 

## Slide 13: Class II Organic Solvents
Tetrachloroethylene Cl₂C=CCl₂ CAS RN:127-18-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Airway disorders, Central nervous system disorders, Peripheral nervous system disorders, Liver disorders, Kidney disorders, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Nausea, Vomiting, General fatigue, Tremor, Sensory abnormalities in limbs, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Facial pallor, Palpitations (rapid heartbeat), Jaundice, Hematuria, Abnormal urination (increased or decreased), Edema, Weight loss | 
Handling Precautions | ・Use only outdoors or in well‑ventilated areas. ・Wash hands thoroughly after handling. ・Do not inhale dust or vapor. ・Do not eat, drink, or smoke in the work area. ・Keep container tightly closed. ・Avoid release into the environment |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene ×, Neoprene 〇 (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and allow rest in a position comfortable for breathing. ・Seek medical attention if feeling unwell. | 
 | If on skin | ・Wash skin with plenty of water and soap. ・Seek medical attention if irritation occurs. ・Remove contaminated clothing and wash it before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy. Continue rinsing. ・Seek medical attention if irritation persists. | 
 | If swallowed | ・Rinse mouth. ・Seek medical attention if feeling unwell. | 

## Slide 14: Class II Organic Solvents
Methyl isobutyl ketone (CH₃)₂CH–CH₂–CO–CH₃ CAS RN:108-10-1 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Airway disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Weight loss | 
Handling Precautions | ・Keep away from heat, high temperatures, sparks, open flames and other ignition sources. ・Keep container tightly closed. ・Take measures to prevent static‐electric discharges. ・Use only outdoors or in well-ventilated areas. ・Wash hands thoroughly after handling. ・Do not inhale dust or vapors. ・Do not eat, drink or smoke in the work area. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. • If exposure has occurred or is suspected, seek medical attention. • If feeling unwell, contact a physician. • Special medical measures may be required. | 
 | If on skin | ・Remove contaminated clothing immediately. ・Wash affected skin with plenty of water or shower. | 
 | If in eyes | ・Rinse carefully with water for several minutes. Remove contact lenses if present and easy to do; continue rinsing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth. • Do not induce vomiting. • Obtain medical examination and treatment. | 

## Slide 15: Class II Organic Solvents
Acetone CH₃–CO–CH₃ CAS RN:67-64-1、666-52-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Pulmonary disorders, Respiratory tract disorders, Gastrointestinal disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Respiratory distress, Chest pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and other ignition sources. ・Keep containers tightly closed. ・Take measures to prevent static-electric discharges. ・Do not inhale dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated areas. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. • If feeling unwell, call a physician. | 
 | If on skin | ・Remove contaminated clothing immediately. ・Rinse with gently running lukewarm water for at least 15 minutes. ・If irritation occurs, seek medical attention. ・If feeling unwell, contact a physician. ・Wash contaminated clothing before reuse. | 
 | If in eyes | ・Remove contact lenses if present and easy to do; continue rinsing. • Rinse eyes with water for several minutes, ensuring thorough flushing. ・If this product gets into the eyes, begin rinsing immediately and flush thoroughly to completely remove the product. Insufficient rinsing may cause irreversible eye injury. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・If feeling unwell, call a physician. • Rinse mouth. • Do not induce vomiting. | 

## Slide 16: Class II Organic Solvents
Isobutyl alcohol (CH₃)₂CH–CH₂OH CAS RN:78-83-1 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static‐electric discharge. ・Avoid inhaling dust or vapor. ・Wash hands thoroughly after handling. ・Use only outdoors or in well-ventilated areas. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene 〇, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | Move victim to fresh air and keep at rest in a comfortable breathing position. | 
 | If on skin | ・Remove contaminated clothing immediately. Wash affected skin under running water or shower. ・If irritation occurs, seek medical attention. | 
 | If in eyes | ・Rinse eyes cautiously with water for several minutes. Remove contact lenses if easy to do; continue rinsing. ・Seek medical attention immediately. | 
 | If swallowed | ・Rinse mouth. Give plenty of water; do not induce vomiting. ・Seek medical attention. | 

## Slide 17: Class II Organic Solvents
Isopropyl alcohol CH₃–CHOH–CH₃ CAS RN:67-63-0 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders, Pulmonary disorders, Liver disorders Splenic disorders, Hematologic disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Chest pain, Dyspnea, Runny nose, Nasal congestion, Nasal/throat pain, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Unsteadiness | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Avoid inhaling dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated areas. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene 〇, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・Seek medical attention and treatment. | 
 | If on skin | ・Wash the affected skin promptly with water. ・Seek medical attention and treatment. ・Remove contaminated clothing and wash before reuse. | 
 | If in eyes | ・Rinse carefully with water for several minutes. Remove contact lenses if present and easy to do; continue rinsing. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Seek medical attention and treatment. ・Rinse mouth. | 

## Slide 18: Class II Organic Solvents
Isopentyl alcohol (CH₃)₂CH–CH₂–CH₂OH CAS RN:123-51-3 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Avoid inhaling dust or vapor. ・Wash hands thoroughly after handling. ・Use only outdoors or in well-ventilated areas. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・If feeling unwell, seek medical attention. ・If symptoms persist, contact a physician. | 
 | If on skin | ・Wash affected area with plenty of water and soap. ・If symptoms persist, contact a physician. | 
 | If in eyes | ・Rinse eyes carefully with water for several minutes. Remove contact lenses if present and easy to do, then continue rinsing. ・Seek medical attention if irritation persists | 
 | If swallowed | Rinse mouth with water. Obtain medical examination immediately. | 

## Slide 19: Class II Organic Solvents
Ethyl ether CH₃CH₂–O–CH₂CH₃ CAS RN:60-29-7 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Respiratory distress | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static‐electric discharge. ・Avoid inhaling dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated areas. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・ Move the person to fresh air and have them rest in a half-sitting position. ・Artificial respiration may be required; contact a medical facility immediately. | 
 | If on skin | ・Remove all contaminated clothing at once. ・Rinse affected skin under running water or shower. | 
 | If in eyes | ・Rinse eyes with plenty of water for several minutes. Remove contact lenses if present and easy to do; continue rinsing. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth; do not induce vomiting. Give 1–2 cups of water. ・If feeling unwell, contact a physician. | 

## Slide 20: Class II Organic Solvents
Ethylene glycol monoethyl ether C₂H₅O–CH₂–CH₂–OH CAS RN:110-80-5 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Liver disorders, Kidney disorders, Hematologic disorders, Suspected reproductive toxicity, Testicular disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Unsteadiness | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static‐electric discharge. ・Avoid inhaling dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated areas. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene △, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・Call a physician if they feel unwell. | 
 | If on skin | ・Remove all contaminated clothing immediately. ・Wash skin thoroughly with water. ・Call a physician if they feel unwell or if irritation occurs. ・Wash contaminated clothing before reuse. | 
 | If in eyes | ・Remove contact lenses if easy to do; continue to rinse eyes with water for several minutes. ・If irritation persists, seek medical attention. | 
 | If swallowed | Rinse mouth promptly. Seek medical examination. | 

## Slide 21: Class II Organic Solvents
Ethylene glycol monoethyl ether acetate CH₃COO–CH₂–CH₂–OC₂H₅ CAS RN:111-15-9 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Liver disorders, Kidney disorders, Hematologic disorders, Suspected reproductive toxicity, Testicular disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Unsteadiness | 
Handling Precautions | ・Keep away from heat, high-temperature surfaces, sparks and open flames. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Use only outdoors or in well-ventilated areas. ・Avoid inhaling dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene △, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air. ・If breathing difficulty occurs, administer oxygen. ・As soon as possible, have them inhale a glucocorticoid aerosol spray with repeated deep breaths. ・Seek medical attention. | 
 | If on skin | ・Remove contaminated clothing at once. ・Rinse affected skin under copious running water for at least 10–20 minutes. ・Seek medical attention. | 
 | If in eyes | ・Rinse eyes with plenty of water for at least 10 minutes; remove contact lenses if easy to do. ・Seek medical attention. | 
 | If swallowed | ・Rinse mouth; if conscious, give a cupful(Approximately 200mL) of water. – Do not induce vomiting. – Seek medical attention. | 

## Slide 22: Class II Organic Solvents
Ethylene glycol mono-n-butyl ether C₄H₉O–CH₂–CH₂–OH CAS RN:111-76-2 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders, Pulmonary disorders, Liver disorders, Kidney disorders, Hematologic disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Chest pain, Dyspnea, Runny nose, Nasal congestion, Nasal/throat pain, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Unsteadiness | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Avoid inhalation of dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Keep container tightly closed. ・Use only outdoors or in well-ventilated areas. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene 〇, Neoprene 〇 (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move victim to fresh air and have them rest in a comfortable position for breathing. ・Call a physician immediately. | 
 | If on skin | ・Wash the area with plenty of water and soap. ・Remove and discard all contaminated clothing; launder before reuse. ・If irritation occurs, seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. ・Remove contact lenses if easy to do; continue rinsing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, call a physician. | 

## Slide 23: Class II Organic Solvents
Ethylene glycol monomethyl ether CH₃O–CH₂–CH₂–OH CAS RN:109-86-4 |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders (ataxia, tremor, etc.), Respiratory tract disorders, Liver disorders, Kidney disorders, Hematologic disorders, Suspected reproductive toxicity, Testicular disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Finger tremor, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Unsteadiness | 
Handling Precautions | ・Keep away from heat, sparks, open flame and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static‐electric discharge. ・Avoid inhaling dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated areas. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air; have them rest in a position comfortable for breathing. ・Contact a physician. Special treatment may be required. | 
 | If on skin | ・Remove all contaminated clothing immediately. Wash skin under running water or shower. ・Wash thoroughly with plenty of water and soap. ・Special treatment may be required. ・If exposure occurs or you feel unwell, seek medical attention. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Rinse eyes with plenty of water for several minutes; remove contact lenses if easy to do. ・Seek medical attention. Special ophthalmic treatment may be required. | 
 | If swallowed | ・Rinse mouth; give plenty of water to drink. ・Special treatment may be required. ・Contact a physician for diagnosis and treatment. | 

## Slide 24: Class II Organic Solvents
o-Dichlorobenzene C6H4Cl2 CAS RN:95-50-1 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Peripheral nervous system disorders, Liver disorders, Kidney disorders, Respiratory tract disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Unsteadiness | 
Handling Precautions | ・Keep away from heat, hot surfaces, sparks, open flames and other ignition sources. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated places. ・Avoid inhaling dust or vapor. ・Keep container tightly closed. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air. ・If breathing is difficult, administer oxygen. ・If breathing has stopped, perform artificial respiration (mouth-nose method first; if impossible, mouth-to-mouth). ・Seek medical attention. | 
 | If on skin | ・Remove and isolate contaminated clothing. ・Wash affected skin thoroughly with plenty of water and soap. ・If irritation occurs, seek medical attention. | 
 | If in eyes | ・Rinse immediately with plenty of water for at least 10 minutes. Remove contact lenses if easy to do and continue rinsing. ・Seek medical attention. | 
 | If swallowed | ・Rinse mouth. If conscious, give 1–2 cups of water or an activated-charcoal suspension (≈3 tbsp in a cup of water). Do not induce vomiting. ・Do not give edible oils, castor oil, milk or alcohol. ・Seek medical attention. | 

## Slide 25: Class II Organic Solvents
Xylene C₆H₄(CH₃)₂ CAS RN:1330-20-7、95-47-6、108-38-3、106-42-3 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Liver disorders, Kidney disorders, Respiratory tract disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated areas. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the victim to fresh air and have them rest in a comfortable breathing position. ・Obtain medical attention and diagnosis. ・If feeling unwell, seek medical attention and diagnosis from a physician. | 
 | If on skin | ・Remove contaminated clothing. ・Rinse skin immediately with plenty of water and wash with soap. ・Obtain medical attention and diagnosis. ・Wash contaminated clothing before reuse. | 
 | If in eyes | ・Rinse eyes with water for several minutes, removing contact lenses if easy to do; continue rinsing. ・Obtain medical attention and diagnosis. | 
 | If swallowed | ・Rinse mouth. ・Obtain medical attention and diagnosis. | 

## Slide 26: Class II Organic Solvents
Cresol C₆H₄–CH₃–OH CAS RN:1319-77-3、95-48-7、108-39-4、106-44-5 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders, Pulmonary disorders, Liver disorders, Kidney disorders, Hematologic disorders, Cardiovascular disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Heavy-headedness, Dizziness, Drowsiness, Vomiting, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Dyspnea, Chest pain, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated areas. ・Keep container tightly closed. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene 〇, Neoprene 〇 (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move victim to fresh air and have them rest in a position comfortable for breathing. ・Call a physician immediately. ・If feeling unwell, seek medical attention. | 
 | If on skin | ・Remove contaminated clothing immediately. ・Contact a physician immediately. ・Wash the skin promptly. ・Rinse the skin with running water or take a shower. ・If feeling unwell, seek medical. ・Wash contaminated clothing before reuse. | 
 | If in eyes | ・Contact a physician immediately. ・Rinse eyes cautiously with water for several minutes. Remove contact lenses if easy to do and continue rinsing. ・If feeling unwell, seek medical attention. | 
 | If swallowed | ・Contact a physician immediately. ・Rinse mouth. Do not induce vomiting. ・If feeling unwell, seek medical attention. | 

## Slide 27: Class II Organic Solvents
Chlorobenzene C6H5Cl CAS RN:108-90-7 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Peripheral nervous system disorders, Liver disorders, Kidney disorders, Hematologic disorders, Endocrine disorders (adrenal), Suspected carcinogenicity, Systemic toxicity (multi-organ effects possible; no single target organ identified) | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory disturbances of limbs, Motor impairment of limbs, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Dyspnea, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Unsteadiness, Weight loss | 
Handling Precautions | ・Do not eat, drink or smoke in the work area. ・Keep away from heat, sparks, open flames and hot surfaces. ・Use only outdoors or in well-ventilated areas. ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Keep container tightly closed. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep the person comfortable position for breathing. ・Call a physician immediately. | 
 | If on skin | ・Remove contaminated clothing and launder before reuse. ・Wash skin promptly with plenty of soap and water. ・If feeling unwell, call a physician. ・Wash clothing before reuse to remove contamination. | 
 | If in eyes | ・Remove contact lenses if easy to do; continue rinsing. ・Rinse eyes with water for several minutes. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth. Call a physician immediately. ・Do not induce vomiting. | 

## Slide 28: Class II Organic Solvents
Isobutyl acetate CH3COOCH2CH(CH3)2 CAS RN:110-19-0 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Avoid inhalation of dust or vapors. ・Wash hands thoroughly after handling. ・Use only outdoors or in well-ventilated areas. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・If symptoms (e.g. feeling unwell) occur, call a physician. | 
 | If on skin | ・If irritation develops, seek medical attention. ・If feeling unwell, call a physician. ・Wash contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. ・Remove contact lenses if easy to do and continue rinsing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | Rinse mouth. If feeling unwell, call a physician. | 

## Slide 29: Class II Organic Solvents
Isopropyl acetate CH3COOCH(CH3)2 CAS RN:108-21-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Avoid inhalation of dust or vapor. ・Wash hands thoroughly after handling. ・Use only outdoors or in well-ventilated areas. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep the person comfortable for breathing position. ・If feeling unwell, seek medical attention. | 
 | If on skin | ・Rinse the skin promptly. ・If irritation develops, seek medical attention. ・If feeling unwell, call a physician. ・Wash contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes, removing contact lenses if easy to do; continue rinsing. ・If eye irritation persists, obtain medical diagnosis and treatment. | 
 | If swallowed | Rinse mouth promptly. Seek medical diagnosis and treatment. | 

## Slide 30: Class II Organic Solvents
Isopentyl acetate CH3COO(CH2)2CH(CH3)2 CAS RN:123-92-2 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Peripheral nervous system disorders(optic nerve), Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated places. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep the person comfortable for breathing position. ・If feeling unwell, call a physician. | 
 | If on skin | ・Rinse the skin promptly. ・If feeling unwell, call a physician. ・Wash contaminated clothing before reuse. ・If skin irritation occurs, seek medical diagnosis and treatment. | 
 | If in eyes | ・Remove contact lenses if easy to do; continue rinsing. ・Rinse eyes with water for several minutes. ・If eye irritation persists, seek medical diagnosis and treatment. | 
 | If swallowed | Rinse mouth immediately. Seek medical diagnosis and treatment. | 

## Slide 31: Class II Organic Solvents
Ethyl acetate CH3COOCH2CH3 CAS RN:141-78-6 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, hot surfaces, sparks, open flames and other ignition sources. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Avoid inhalation of dust or vapors. ・Wash hands thoroughly after handling. ・Use only outdoors or in well-ventilated places. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. ・If feeling unwell, seek medical attention. | 
 | If on skin | ・Remove contaminated clothing immediately. ・Wash affected skin with water or shower. | 
 | If in eyes | ・Rinse cautiously with water for several minutes; remove contact lenses if easy to do, then continue rinsing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, seek medical attention. | 

## Slide 32: Class II Organic Solvents
Butyl acetate CH₃COO–CH₂CH₂CH₂CH₃ CAS RN:123-86-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Wash hands thoroughly after handling. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. ・Call a physician immediately. | 
 | If on skin | ・Remove all contaminated clothing immediately. ・Wash affected skin with plenty of water or by showering. ・If feeling unwell, call a physician. | 
 | If in eyes | ・Rinse cautiously with water for several minutes; remove contact lenses if easy to do, then continue rinsing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, call a physician. | 

## Slide 33: Class II Organic Solvents
n-Propyl acetate CH3COO(CH2)2CH3 CAS RN:109-60-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Avoid inhalation of dust or vapors. ・Wash hands thoroughly after handling. ・Use only outdoors or in well-ventilated areas. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・If feeling unwell, call a physician. | 
 | If on skin | ・Remove all contaminated clothing immediately. ・Rinse the affected skin promptly. ・Wash contaminated clothing before reuse. ・If feeling unwell or if irritation occurs, seek medical diagnosis and treatment. | 
 | If in eyes | ・Remove contact lenses if easy to do, then continue rinsing. ・Rinse cautiously with water for several minutes. ・If eye irritation persists, seek medical diagnosis and treatment. | 
 | If swallowed | ・Rinse mouth. ・Do not give anything to an unconscious person. ・Call a physician immediately. ・ Do not induce vomiting unless directed by a medical professional. | 

## Slide 34: Class II Organic Solvents
n-Pentyl acetate CH3COO(CH2)4CH3 CAS RN:628-63-7 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Peripheral nervous system disorders(optic nerve), Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Avoid inhalation of dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated places. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. ・Call a physician immediately. | 
 | If on skin | ・Rinse the skin promptly. ・If skin irritation seek medical diagnosis and treatment. ・Remove and launder contaminated clothing before reuse. | 
 | If in eyes | ・Remove contact lenses if easy to do, then continue rinsing. ・Rinse cautiously with water for several minutes. ・If eye irritation persists, seek medical diagnosis and treatment. | 
 | If swallowed | ・Rinse mouth. ・Do not give anything to an unconscious person. ・Call a physician immediately. ・Do not induce vomiting unless directed by a medical professional. | 

## Slide 35: Class II Organic Solvents
Methyl acetate CH3COOCH3 CAS RN:79-20-9 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Peripheral nervous system disorders(optic nerve), Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory disturbances of the limbs, Motor impairment of the limbs, Visual disturbances, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take precautions against static-electric discharge. ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated places. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the affected person to fresh air and have them rest in a comfortable breathing position. ・If they feel unwell, call a physician. | 
 | If on skin | ・Rinse the area with lukewarm running water, then wash thoroughly with soap. ・If they feel unwell or if skin irritation occurs, seek medical diagnosis and treatment. | 
 | If in eyes | ・Remove contact lenses if easy to do and continue rinsing. ・Rinse cautiously with water for several minutes. ・If eye irritation persists, seek medical diagnosis and treatment. | 
 | If swallowed | ・Rinse mouth. ・Do not give anything to an unconscious person. ・Call a physician immediately. ・Do not induce vomiting unless directed by medical personnel. | 

## Slide 36: Class II Organic Solvents
Cyclohexanol C6H11OH CAS RN:108-93-0 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Peripheral nervous system disorders, Cardiovascular disorders Respiratory tract disorders, Liver disorders, Kidney disorders, Male reproductive disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema | 
Handling Precautions | ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated places. ・Keep container tightly closed. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile 〇, Latex ×, Chloroprene △, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. ・Artificial respiration may be necessary. ・Seek medical attention. | 
 | If on skin | ・Wash affected area thoroughly with plenty of water and soap. ・If skin irritation occurs, seek medical diagnosis and treatment. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. ・Seek medical attention immediately. | 
 | If swallowed | ・Rinse mouth. Give 1–2 glasses of water to drink. ・Seek medical attention. | 

## Slide 37: Class II Organic Solvents
Cyclohexanone O=(CH₂)₅ CAS RN:108-94-1 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system disorders, Respiratory tract disorders, Bone abnormalities, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Eczema, Hives, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion. Nasal/throat pain, Bone pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces ・Keep container tightly closed ・Take measures to prevent static-electric discharge ・Wash hands thoroughly after handling ・Do not eat, drink or smoke in the work area ・Use only outdoors or in well-ventilated locations ・Do not remove contaminated work clothes from the work area ・Avoid inhalation of dust or vapor |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and have them rest in a comfortable breathing position ・Call a physician immediately. | 
 | If on skin | ・Immediately remove contaminated clothing. ・Rinse the skin under running water or shower, then wash with plenty of soap and water. ・Wash contaminated clothing before reuse. ・If irritation occurs, seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes; remove contact lenses if easy to do, then continue rinsing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・If feeling unwell, call a physician immediately. ・Rinse mouth. | 

## Slide 38: Class II Organic Solvents
N,N-Dimethylformamide HCON(CH₃)₂ CAS RN:68-12-2、4472-41-7 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders, Liver disorders, Digestive system disorders, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Easy fatigability, Jaundice, Abdominal pain, Diarrhea, Loss of appetite, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flames and other ignition sources. ・Keep container tightly closed. ・Take precautions against static-electric discharge. ・Use only outdoors or in well-ventilated places. ・Wash hands thoroughly after handling. ・Do not inhale dust or vapors. ・Do not eat, drink or smoke in the work area. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and have them rest in a comfortable breathing position. ・Give oxygen if breathing is difficult. ・Contact a medical facility immediately. ・As soon as possible and repeatedly, have the victim inhale a glucocorticoid spray deeply. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Rinse affected skin under running water or shower, then wash thoroughly with water and soap. ・Do NOT use alcohol, gasoline or other solvents. ・Place contaminated clothing in a sealed container. ・If skin irritation occurs, seek medical diagnosis and treatment. | 
 | If in eyes | ・Hold eyelids wide open and rinse the eye with running water for at least 10 minutes. ・If eye irritation persists, seek medical diagnosis and treatment. | 
 | If swallowed | ・If conscious, give 1–2 glasses of water to drink. ・If spontaneous vomiting occurs, position the head lower than the chest and on the side to prevent aspiration. | 

## Slide 39: Class II Organic Solvents
Tetrahydrofuran O–(CH₂)₄ CAS RN:109-99-9、1693-74-9 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders, Liver disorders, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Easy fatigability, Jaundice, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take precautions against static-electric discharge. ・Wear chemical-resistant gloves, protective clothing, safety goggles and face shield. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated places. ・Do not inhale dust or vapors. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. ・If they feel unwell, call a physician. | 
 | If on skin | ・Rinse affected skin promptly under running water. ・Remove contaminated clothing and launder before reuse. ・If they feel unwell, call a physician. | 
 | If in eyes | ・Rinse cautiously with water for several minutes; remove contact lenses if easy to do and continue rinsing. ・If eye irritation persists, seek medical diagnosis and treatment. | 
 | If swallowed | ・Call a physician immediately. ・Rinse mouth. | 

## Slide 40: Class II Organic Solvents
1,1,1-Trichloroethane CCl₃–CH₃ CAS RN:71-55-6 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders(e.g., impaired coordination), Cardiovascular disorders(arrhythmias), Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Weight loss, Arrhythmias | 
Handling Precautions | ・Wash hands thoroughly after handling. ・Wear protective gloves, protective clothing, safety goggles and face shield. ・Do not inhale dust or vapors. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated locations. ・Keep container tightly closed. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・If they feel unwell, contact a physician. | 
 | If on skin | ・Wash the area with plenty of water and soap. ・Remove contaminated clothing. ・If skin irritation occurs, seek medical diagnosis and treatment. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes; remove contact lenses if easy to do, then continue rinsing. ・If eye irritation persists, seek medical diagnosis and treatment. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, seek medical diagnosis and treatment. | 

## Slide 41: Class II Organic Solvents
Toluene C₆H₅–CH₃ CAS RN:108-88-3、2037-26-5 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders, Kidney disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Intoxication, Tremors, Ataxia, Altered consciousness, Memory impairment, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Hematuria, Polyuria, Oliguria, Edema | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take precautions against static-electric discharge. ・Do not inhale dust, smoke or vapor. ・Avoid contact during pregnancy or breastfeeding. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated locations. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep the person comfortable for breathing. Keep rest ・Seek medical diagnosis and treatment. ・Requires special medical attention. | 
 | If on skin | ・Wash affected skin thoroughly with plenty of water and soap. ・Seek medical diagnosis and treatment. ・Requires special medical attention. ・Remove contaminated clothing; launder before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes; remove contact lenses if easy to do, then continue rinsing. ・Seek medical diagnosis and treatment. ・Requires special medical attention. | 
 | If swallowed | ・Seek medical diagnosis and treatment immediately. ・Requires special medical attention. ・Do not induce vomiting (volatile liquid—vomiting may increase aspiration risk). Rinse mouth; water may be given to rinse. ・If unconscious, do not give anything by mouth. | 

## Slide 42: Class II Organic Solvents
n-Hexane C6H14 CAS RN:110-54-3 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Peripheral nervous system disorders, Respiratory tract disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory disturbances of the limbs, Motor dysfunction of the limbs, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, hot surfaces, sparks, open flames and other ignition sources. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Wash hands thoroughly after handling. ・Use only outdoors or in well-ventilated places. ・Do not inhale dust or vapors. ・Do not eat, drink or smoke in the work area. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene △, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air. ・If breathing is difficult, administer oxygen. ・Seek medical attention. | 
 | If on skin | ・Remove contaminated clothing. ・Wash affected skin area thoroughly with plenty of water and soap. ・Seek medical attention. | 
 | If in eyes | ・Rinse eyes with running water for at least 10 minutes; remove contact lenses if easy to do, then continue rinsing ・Seek medical attention. | 
 | If swallowed | ・Rinse mouth. Do not induce vomiting. ・Seek medical examination and treatment immediately. | 

## Slide 43: Class II Organic Solvents
1-Butanol CH₃–CH₂–CH₂–CH₂OH CAS RN:71-36-3 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Auditory disorders, Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Hearing impairment, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, hot surfaces, sparks, open flames and other ignition sources. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge ・Wash hands thoroughly after handling ・Use only outdoors or in well-ventilated areas. ・Do not inhale dust or vapors. ・Do not eat, drink or smoke in the work area. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air. ・If breathing is difficult, administer oxygen. ・If breathing stops, perform rescue breathing (mouth-to-nose, or mouth-to-mouth if necessary). ・Seek medical attention. | 
 | If on skin | ・Remove contaminated clothing. ・Rinse affected skin under running water for at least 10–20 minutes ・Seek medical attention. | 
 | If in eyes | ・ Flush eyes with water for at least 10 minutes; remove contact lenses if easy to do, then continue rinsing ・Seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・If conscious, give 1–2 glasses of water; do not induce vomiting ・Seek medical attention. | 

## Slide 44: Class II Organic Solvents
2-Butanol CH₃–CHOH–CH₂–CH₃ CAS RN:78-92-2 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat irritation | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take precautions against static-electric discharge. ・Avoid inhaling dust or vapors. ・Wash hands thoroughly after handling. ・Use only outdoors or in a well-ventilated location. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex △, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and let them rest in a position comfortable for breathing. ・Seek medical attention. | 
 | If on skin | ・Wash the skin promptly. ・Remove contaminated clothing; launder before reuse. ・Seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes; if wearing contact lenses and they can be removed easily, remove them and continue rinsing. ・ If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Seek medical attention. ・Rinse mouth. | 

## Slide 45: Class II Organic Solvents
Methanol CH₃OH CAS RN:67-56-1 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Optic nerve disorders, Respiratory tract disorders, Pulmonary disorders, Suspected reproductive toxicity, Systemic toxicity(effects on multiple organs) | 
 | Symptoms | Eye pain, tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory disturbances of the limbs, Motor dysfunction of the limbs, Visual disturbances, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Respiratory distress | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Use tools that do not spark. ・Do not eat, drink or smoke in the work area. ・Wash hands thoroughly after handling. ・Use only outdoors or in well-ventilated locations. ・Avoid inhalation of dust or vapor. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene △, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Seek medical attention. ・Move to fresh air and have the person rest in a comfortable breathing position. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Rinse skin with plenty of water or shower. ・Seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・Seek medical attention. | 

## Slide 46: Class II Organic Solvents
Methyl ethyl ketone CH₃–CO–CH₂–CH₃ CAS RN:78-93-3 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders, Kidney disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Hematuria, Polyuria, Oliguria, Edema, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take precautions against static-electric discharge. ・Avoid inhalation of dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in well-ventilated locations. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and have them rest in a comfortable position for breathing. ・If feel unwell, seek medical attention. ・Special medical measures may be required. | 
 | If on skin | ・Promptly rinse the affected skin with water and wash with soap. ・Remove and launder contaminated clothing before reuse. ・Seek medical attention. ・Special medical measures may be required. | 
 | If in eyes | ・Rinse cautiously with water for several minutes, holding eyelids open; remove contact lenses if easy to do and continue rinsing. ・If eye irritation persists, seek medical attention. ・Special medical measures may be required. | 
 | If swallowed | ・Seek medical examination and treatment immediately. ・Rinse mouth. ・Special medical measures may be required. | 

## Slide 47: Class II Organic Solvents
Methyl cyclohexanol CH3-C6H11OH CAS RN:25639-42-3 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Heavy-headedness, Dizziness, Drowsiness, Vomiting, General fatigue | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take measures to prevent static-electric discharge. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Avoid inhalation of dust or vapors. ・Use only outdoors or in well-ventilated locations. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ○, Latex ×, Chloroprene △, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and rest in a comfortable breathing position. ・If feeling unwell, seek medical attention. | 
 | If on skin | ・Wash affected area with plenty of water and soap. ・Remove and launder contaminated clothing before reuse. ・If skin irritation occurs or feel unwell, seek medical attention for diagnosis and treatment. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. ・If irritation persists or feel unwell, seek medical attention. | 
 | If swallowed | ・If feel unwell seek medical attention. ・Rinse mouth. | 

## Slide 48: Class II Organic Solvents
Methylcyclohexanone C₆H₉(CH₃)–CO CAS RN:1331-22-2 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, hot surfaces, sparks, open flames and other ignition sources. ・Keep container tightly closed. ・Take measures to prevent static‐electric discharge. ・Avoid inhaling dust or vapor. ・Wash hands thoroughly after handling. ・Use only outdoors or in a well-ventilated area. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep the person comfortable for breathing. ・If feeling unwell, seek medical attention. | 
 | If on skin | ・Immediately remove all contaminated clothing. Rinse the affected skin with water or shower thoroughly. ・If skin irritation develops, seek medical attention | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth; do not induce vomiting ・If conscious, give small sips of water. ・Keep the person warm and at rest. ・If feeling unwell, seek medical attention immediately | 

## Slide 49: Class II Organic Solvents
2-Methyl-n-butylketone CH₃–CO–CH₂–CH₂–CH₂–CH₃ CAS RN:591-78-6 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders, Peripheral nervous system disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory disturbances of the limbs, Motor dysfunction of the limbs, Weakness, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces (ignition sources). ・Keep container tightly closed. ・Take measures to prevent static‐electric discharge. ・Avoid inhalation of dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well‐ventilated location. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas where high vapor levels may occur, such as third‑control‑area zones or locations where vapors escape due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・If you feel unwell, seek medical attention. ・If symptoms persist, contact a physician. | 
 | If on skin | ・Wash the affected area with plenty of water. ・If symptoms persist, contact a physician. | 
 | If in eyes | ・Rinse cautiously with water for 15–20 minutes. Remove contact lenses if easy to do, then continue rinsing. ・If symptoms persist, contact a physician. | 
 | If swallowed | Rinse mouth with water. Seek medical examination immediately. | 

## Slide 50: Class III Organic Solvents
Gasoline Chemical formula: not specified CAS RN:8006-61-9 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Lung disorders, Kidney disorders, Circulatory system disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Hematuria, Polyuria, Oliguria, Edema, Chest pain, Difficulty breathing, Shortness of breath, Weight loss | 
Handling Precautions | ・Do not eat, drink or smoke in the work area. ・Keep away from heat, sparks, open flames and hot surfaces(ignition sources). ・Prevent static‐electric discharge or sparks. ・Use personal protective equipment and local exhaust or other ventilation to minimize exposure. ・Use only outdoors or in a well-ventilated area. ・Avoid inhaling vapors. ・Keep container tightly closed. ・Wash hands thoroughly after handling. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene △, Neoprene ○ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. ・Seek medical attention. ・If feeling unwell, continue to monitor and arrange medical care. | 
 | If on skin | ・Remove contaminated clothing. ・Rinse skin thoroughly with plenty of water and soap immediately. ・Seek medical attention. ・Wash contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. ・Seek medical examination and treatment | 
 | If swallowed | ・Rinse mouth. ・Seek medical attention. | 

## Slide 51: Class III Organic Solvents
Solvent naphtha (coal) Chemical formula: not specified CAS RN:65996-79-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take precautions against static-electric discharge. ・Use tools that do not generate sparks. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene △, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・If feeling unwell, seek medical attention. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Rinse affected skin thoroughly with water or shower. | 
 | If in eyes | ・If irritation persists, seek medical attention. ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, seek medical attention. | 

## Slide 52: Class III Organic Solvents
Petroleum Ether Chemical formula: not specified CAS RN: not specified |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders. Skin disorders, Central nervous system disorders, Peripheral nervous system disorders, Respiratory tract disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Take measures to prevent static-electric discharge. ・Use non-sparking tools. ・Avoid inhalation of vapors, dust or mist. ・Use only outdoors or in a well-ventilated area. ・Keep container tightly closed. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and have rest in a comfortable position for breathing. ・If feeling unwell, seek medical attention. | 
 | If on skin | ・Rinse the affected area immediately with plenty of water and soap. ・If irritation or discomfort persists, seek medical attention. ・If feeling unwell, seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. ・If eye irritation continues or if feeling unwell, seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, seek medical attention. ・Do not induce vomiting. | 

## Slide 53: Class III Organic Solvents
Solvent naphtha (petroleum), light arom Chemical formula: not specified CAS RN:64742-95-6 |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Respiratory tract disorders | 
 | Symptoms | Dermatitis, Pruritus, Skin redness, Headache, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces (ignition sources). ・Keep containers tightly closed. ・Take measures to prevent static‐electric discharge. ・Use tools that do not generate sparks. ・Wash hands thoroughly after handling. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | If feeling unwell, seek medical attention. | 
 | If on skin | ・Wash contaminated clothing before reuse. ・Remove contaminated clothing immediately. ・Wash the affected skin with plenty of water and soap. ・If skin irritation occurs, seek medical attention for diagnosis and treatment. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Call a doctor immediately. ・Do not induce vomiting. | 

## Slide 54: Class III Organic Solvents
Petroleum Benzine Chemical formula: not specified CAS RN:8032-32-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Peripheral nervous system disorders | 
 | Symptoms | Sensory disturbances of the limbs, Motor dysfunction of the limbs, Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take precautions against static-electric discharge. ・Use non-sparking tools. ・Do not eat, drink or smoke in the work area. ・Wash hands thoroughly after handling. ・Use only outdoors or in a well-ventilated location. ・Avoid inhalation of dust or vapors. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene △, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・If feeling unwell, contact a physician. ・Move to fresh air and rest in a comfortable breathing position. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Rinse skin with running water or shower; wash with plenty of water and soap. ・Wash contaminated clothing before reuse. ・ Seek medical attention if irritation occurs. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Immediately contact a physician. ・Do not induce vomiting. | 

## Slide 55: Class III Organic Solvents
Turpentine oil Chemical formula: not specified CAS RN:8006-64-2 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system disorders, Respiratory tract disorders, Kidney disorders, Hematologic (blood) disorders, Urinary system disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Eczema, Urticaria, Hives, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Blood in urine, increased or decreased urine output, edema, Polyuria, Oliguria, Edema, Urinary frequency, Dysuria, Lower abdominal pain, Sensation of residual urine, Facial pallor, Rapid heartbeat(Palpitations), Unsteadiness | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep the container tightly closed. ・Use tools that do not generate sparks. ・Take precautions against static‐electric discharge. ・Avoid inhaling vapors or dust. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated location. ・Do not remove contaminated work clothing from the work area. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene ×, Neoprene ○ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・Seek medical attention. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Rinse affected skin thoroughly with water or shower. ・If irritation or rash develops, seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Do not induce vomiting. Give one to two cups of water to drink. ・Seek medical attention immediately. | 

## Slide 56: Class III Organic Solvents
Mineral spirit Chemical formula: not specified CAS RN:64742-47-8、8052-41-3 |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Central nervous system disorders, Respiratory tract disorders, Liver disorders, Testicular disorders | 
 | Symptoms | Dermatitis, Pruritus(Itching), Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Easy fatigability, Jaundice | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Take measures to prevent static-electric discharge. ・Use non-sparking tools. ・Avoid inhalation of dust or vapors. ・Wash hands thoroughly after handling. ・Use only outdoors or in a well-ventilated area. ・Keep container tightly closed. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene △, Neoprene ○ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures | If inhaled | ・Move the affected person to fresh air and have them rest in a comfortable position for breathing. ・If they feel unwell, seek medical attention. | 
 | If on skin | ・Remove contaminated clothing. ・Wash the affected skin promptly with plenty of water and soap. ・If irritation occurs or the person feels unwell, seek medical attention. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. ・If irritation persists or the person feels unwell, seek medical attention. | 
 | If swallowed | ・Do not induce vomiting. ・Rinse mouth. ・If feeling unwell, seek medical attention. | 

## Slide 57: Class I Specified Chemical Substances
α-Naphthylamine and its salts C₁₀H₆NH₂ CAS RN:134-32-7,552-46-5,etc. |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Hematopoietic(blood) disorders, Urinary system disorders, Urinary tract tumors | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Facial pallor, Palpitations(Tachycardia)、Headache, Nausea, Impaired consciousness, Cyanosis, Dizziness, Unsteadiness, Hematuria, Polyuria, Oliguria, Edema, Frequent urination, Dysuria, Discomfort during urination, Discomfort during urination, Sensation of residual urine, General fatigue, Weight loss | 
Handling Precautions (α-Naphthylamine) | ・Avoid inhalation of dust or vapors. ・Do not eat, drink or smoke in the work area. ・Keep containers tightly closed. ・Wash hands thoroughly after handling. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures (α-Naphthylamine) | If inhaled | ・Move the person to fresh air; have them rest in a position comfortable for breathing. ・If they feel unwell, seek medical attention. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Wash the affected skin promptly with plenty of water. ・Gently wash with ample soap and water. ・If discomfort persists, seek medical attention. ・Discard contaminated clothing and shoes. | 
 | If in eyes | ・Remove contact lenses if worn and easy to do, then continue rinsing. ・Rinse eyes with water for several minutes, holding eyelids open. ・If eye irritation persists, obtain medical advice or treatment. | 
 | If swallowed | Rinse mouth promptly. Seek medical attention. | 

## Slide 58: Class I Specified Chemical Substances
Polychlorinated biphenyls (PCB) C12H10-nCln CAS RN:1336-36-3,11097-69-1,53469-21-9,etc. |  |  | 
Health Hazards | Possible Diseases | Skin disorders(e.g. chloracne), Respiratory tract disorders, Liver disorders, Gastrointestinal disorders, Hematologic(blood) disorders, Immune system disorders, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye discharge, Conjunctival redness, Nail discoloration and deformity, Dermatitis, Pruritus(Itching), Skin redness, Acne(Pimples), General fatigue, Easy fatigability, Jaundice, Abdominal pain, Diarrhea, Vomiting, Loss of appetite, Facial pallor, Palpitations, Dizziness, Unsteadiness, Weight loss | 
Handling Precautions | ・Do not eat, drink or smoke in the work area. ・Use appropriate personal protective equipment and local exhaust or general ventilation to minimize exposure. ・Work only outdoors or in a well-ventilated area. ・Avoid inhalation of dust or vapors. ・Wash hands thoroughly after handling. ・Keep containers tightly closed. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene 〇, Neoprene 〇 (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Use an organic-gas/organic-vapor cartridge respirator with particulate filter (consult the PPE manufacturer for specific models).
First Aid Measures | If inhaled | ・Move the person to fresh air and have them rest in a comfortable position for breathing. ・If they feel unwell, summon medical attention. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Gently wash the affected skin with plenty of soap and water. ・If feeling unwell, seek medical attention. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Remove contact lenses if easy to do, then continue rinsing. ・Rinse eyes cautiously with water for several minutes. ・If eye irritation persists, obtain medical advice or treatment. | 
 | If swallowed | Rinse mouth promptly. Seek medical attention. | 

## Slide 59: Class I Specified Chemical Substances
o-Tolidine and its salts CH₃–C₆H₃(NH₂)₂–CH₃ CAS RN:119-93-7,612-82-8,etc. |  |  | 
Health Hazards | Possible Diseases | Liver disorders, Kidney disorders, Hematologic(blood) disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Dizziness, Unsteadiness, Shortness of breath, Painful urination, Discomfort during urination, Lower abdominal pain, Sensation of residual urine, Weight loss | 
Handling Precautions (o-Tolidine) | ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Avoid inhalation of dust or vapors. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measures (o-Tolidine) | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. ・Obtain medical attention. | 
 | If on skin | ・Wash affected skin promptly with water. ・Seek medical attention. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Remove contact lenses if easy to do, then continue rinsing. ・Rinse cautiously with water for several minutes. ・Obtain medical attention. | 
 | If swallowed | Rinse mouth immediately. Obtain medical attention. | 

## Slide 60: Class I Specified Chemical Substances
Dianisidine and its salts H₃CO–C₆H₃(NH₂)–OCH₃ CAS RN:119-90-4,20325-40-0,etc. |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Respiratory tract disorders, Liver disorders, Hematologic(blood) disorders, Urinary system disorders, Urinary tract tumors | 
 | Symptoms | Dermatitis, Pruritus(Itching), Skin redness, Mucous-membrane irritation, Cough, General fatigue, Easy fatigability, Jaundice, Facial pallor, Palpitations(Tachycardia), Dizziness, Unsteadiness, Shortness of breath, Hematuria, Frequent urination, Painful urination, Lower abdominal pain, Dysuria, Sensation of residual urine, Weight loss | 
Handling Precautions (Dianisidine) | ・Avoid inhalation of dust or vapors. ・Do not eat, drink, or smoke in the work area. ・Keep containers tightly closed. ・Wash hands thoroughly after handling. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Dianisidine) | If inhaled | Move the person to fresh air and have them rest in a position comfortable for breathing. | 
 | If on skin | ・Remove contaminated clothing. ・Rinse the affected skin, then wash thoroughly with soap and water. | 
 | If in eyes | Rinse cautiously with plenty of water for several minutes, removing contact lenses if easy to do. Obtain medical evaluation if irritation persists. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, seek medical attention. | 

## Slide 61: Class I Specified Chemical Substances
Dichlorobenzidine and its salts NH2ClC6H3C6H3ClNH2 CAS RN:91-94-1,612-83-9,etc. |  |  | 
Health Hazards | Possible Diseases | Urinary tract disorders, Urinary tract tumors | 
 | Symptoms | Dermatitis, Headache, Dizziness, Cough, Respiratory irritation, Sore throat, Hematuria, Polyuria, Oliguria, Edema, Frequent urination, Painful urination, Dysuria, Lower abdominal pain, Sensation of residual urine, General fatigue, Weight loss | 
Handling Precautions (Dichlorobenzidine) | ・Use appropriate personal protective equipment and local exhaust or general ventilation to avoid exposure. ・Handle only outdoors or in a well-ventilated area. ・Avoid inhalation of dust. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Dichlorobenzidine) | If inhaled | Move the person to fresh air and have them rest in a position comfortable for breathing. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Rinse the affected skin promptly with plenty of water. ・If feeling unwell or irritation persists, seek medical attention. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Remove contact lenses if easy to do, then continue rinsing. ・Rinse cautiously with water for several minutes. ・If eye irritation persists, obtain medical advice or treatment. | 
 | If swallowed | Rinse mouth promptly. Seek medical attention. | 

## Slide 62: Class I Specified Chemical Substances
Beryllium and its compounds Be CAS RN:7440-41-7,1304-56-9, 13327-32-7,7787-56-6,7787-49-7,etc. |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Airway and pulmonary disorders(e.g. berylliosis) , Respiratory sensitization, Respiratory tract tumors(e.g. lung cancer) | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Skin ulcers, Eczema, Hives, Cough, Shortness of breath, Chest pain, Difficulty breathing, Asthma-like attacks, Chest discomfort, Runny nose, Nasal congestion, Nasal/throat pain, General fatigue, Weight loss | 
Handling Precautions (Beryllium) | ・Do not eat, drink or smoke in the work area. ・If ventilation is inadequate, wear respiratory protective equipment. ・Use personal protective equipment and local/exhaust ventilation to minimize exposure. ・Avoid inhaling dust or fumes. ・Wash hands thoroughly after handling. ・Do not remove contaminated work clothing from the work area. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Beryllium) | If inhaled | ・If breathing is difficult, move the person to fresh air and have them rest in a comfortable position. ・Obtain medical examination and treatment. ・If respiratory symptoms appear, contact a physician. | 
 | If on skin | ・Wash the affected area thoroughly with plenty of water and soap. ・Obtain medical examination and treatment. ・If skin irritation or rash occurs, seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. ・If feeling unwell, obtain medical examination and treatment. | 
 | If swallowed | ・Rinse mouth. ・Obtain medical examination and treatment. | 

## Slide 63: Class I Specified Chemical Substances
Benzotrichloride C6H5CCl3 CAS RN:98-07-7 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders, Sinusitis, Liver disorders, Kidney disorders, Hematologic disorders, Lung cancer, Endocrine disorders(thyroid), Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Nosebleed, Loss of smell, Pain around cheeks, nose, forehead, Facial or eyelid swelling, Fever, Nasal polyps, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, Cough, Sputum, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Chest pain, Enlarged cervical lymph nodes, Weight loss | 
Handling Precautions | ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Avoid inhalation of dust or vapor. ・Use only outdoors or in a well-ventilated area. ・If ventilation is inadequate, wear respiratory protection. ・Do not remove contaminated work clothing from the work area. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile: no data, Latex: no data, Chloroprene: no data, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Use an organic-gas/vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Call a physician. ・If unconscious but breathing, place on their side in a stable position and protect from hypothermia. ・If breathing is difficult, administer oxygen. ・If respiratory irritation occurs, consider inhaled glucocorticoid spray(per medical advice). ・Move to fresh air and have them rest in a comfortable position. ・Seek medical attention if symptoms develop. | 
 | If on skin | ・Seek medical attention if irritation or rash occurs. ・Protect yourself and remove the victim from the source. ・Immediately remove all contaminated clothing. ・Rinse exposed skin under running water or shower, then wash thoroughly with soap and water. ・Do not use alcohol, gasoline or other solvents. | 
 | If in eyes | ・Protect the uninjured eye, then flush the injured eye with water for at least 10 minutes, holding the eyelids open. ・Seek medical attention if irritation persists. ・Continue rinsing with saline or water during transport to medical care. | 
 | If swallowed | ・Poisoning symptoms may be delayed. ・If vomiting occurs spontaneously, prevent aspiration by placing the head lower than the chest in a prone position. ・Rinse mouth and spit out any liquid; do not induce vomiting. If conscious, give 1–2 cups of water. | 

## Slide 64: Class II Specified Chemical Substances
Acrylamide CH₂=CH–CONH₂ CAS RN:79-06-1 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system disorders, Peripheral neuropathy, Hematologic(blood) disorders, Carcinogenicity, Suspected reproductive toxicity(male) | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Eczema, Hives, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory loss or motor dysfunction in the limbs, Facial pallor, Palpitations, Unsteadiness, Weight loss | 
Handling Precautions | ・Do not inhale dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Do not remove contaminated work clothing from the workplace. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile: no data, Latex: no data, Chloroprene: no data, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Use an organic-gas/vapor respirator equipped with particulate (dust)-filter capability.(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・If exposure has occurred or is suspected, seek medical attention. ・If feeling unwell, seek medical attention. ・Special medical intervention may be required. | 
 | If on skin | ・Wash the affected area with plenty of water and soap. ・If feeling unwell, contact a physician. ・Special medical intervention may be required. ・If irritation or rash develops, seek medical attention. ・Remove all contaminated clothing immediately; launder before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes, removing contact lenses if easy to do. Continue flushing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Seek immediate medical attention. ・Special medical intervention may be required. ・Rinse mouth thoroughly. | 

## Slide 65: Class II Specified Chemical Substances
Acrylonitrile CH₂=CH–CN CAS RN:107-13-1 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system disorders, Respiratory tract disorders, Liver disorders, Kidney disorders, Hematologic disorders, Carcinogenicity, Suspected reproductive | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Eczema, Urticaria, Headache, Head heaviness, Dizziness, Drowsiness, Nausea, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Nosebleed, Easy fatigability、Jaundice, hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Unsteadiness, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flame and other ignition sources. ・Keep containers tightly closed. ・Take measures to prevent static‐electricity discharge. ・Do not inhale dust or vapor. ・Avoid contact with eyes, skin or clothing. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated location. ・Do not remove contaminated work clothes from the workplace. ・Prevent release to the environment. ・If ventilation is inadequate, wear appropriate respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the affected person to fresh air and have them rest in a comfortable position. ・Obtain medical examination and treatment without delay. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Obtain medical examination and treatment. ・Rinse affected skin promptly with plenty of water, then wash with soap. ・Launder clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes, removing contact lenses if easy to do. Continue flushing ・Obtain medical examination and treatment. | 
 | If swallowed | ・Obtain medical examination and treatment immediately. ・Rinse mouth thoroughly. | 

## Slide 66: Class II Specified Chemical Substances
Alkyl mercury compounds CnH2n+1Hg CAS RN:593-74-8,627-44-1,etc. |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Central nervous system disorders, Peripheral neuropathy(sensory disturbances of the extremities or perioral area; ataxia; balance disorders; speech disorders; visual or hearing impairment; etc.) | 
 | Symptoms | Dermatitis, Pruritus(Itching), Skin erythema, Headache, Head heaviness, Dizziness, Nausea, Vomiting, General fatigue, Loss of appetite, Poor handwriting(Dysgraphia), Micrographia, Nightmares, Visual impairment, Hearing impairment, Speech disorders, Impaired concentration and memory, Joint pain, Insomnia, Hypersomnia, Depression, Anxiety, Motor and sensory dysfunction, Weight loss | 
Handling Precautions (ジメチル水銀) | ・Keep away from heat, sparks, open flame and high-temperature sources. ・Keep containers tightly closed. ・Take measures to prevent static-electricity discharge. ・Avoid inhalation of dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene: no data (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (ジメチル水銀) | If inhaled | ・If feeling unwell, seek immediate medical examination and treatment. ・If symptoms persist, contact a physician. | 
 | If on skin | ・Wash the affected area thoroughly with copious water. ・If symptoms persist, contact a physician. | 
 | If in eyes | ・Rinse the eye gently under running water for 15–20 minutes, removing contact lenses if easy to do. Continue flushing ・If irritation persists, contact a physician. | 
 | If swallowed | Rinse mouth with water. Seek immediate medical examination and treatment. | 

## Slide 67: Class II Specified Chemical Substances
Indium compounds In CAS RN:1312-41-0,10025-82-8,1312-43-2,13464-82-9,128008-30-0,etc. |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Pulmonary disorders(e.g. interstitial pneumonia), Suspected carcinogenicity | 
 | Symptoms | Dermatitis, Pruritus(Itching), Skin erythema, Eye pain, Tearing, Conjunctival redness, Cough, Sputum production, Shortness of breath, Chest pain, General fatigue, Weight loss | 
Handling Precautions (酸化インジウム) | ・Do not inhale dust or vapor. ・Do not eat, drink, or smoke in the work area. ・Keep containers tightly closed. ・Wash hands thoroughly after handling. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where airborne dust may exceed 0.3 µg/m³ (as determined by workplace monitoring) or during leaks.
 | Type of respiratory protection |  | Use a replaceable‐cartridge particulate respirator rated at RL3 or higher.(It varies depending on the concentration in the air.) (Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (酸化インジウム) | If inhaled | ・Move the affected person to fresh air and have them rest in a position that eases breathing. ・If symptoms persist, seek medical attention. | 
 | If on skin | ・Wash the affected area with plenty of water and soap. ・If symptoms persist, seek medical attention. | 
 | If in eyes | ・Rinse carefully with running water for several minutes, removing contact lenses if easily done. Continue flushing. ・If irritation persists, seek medical attention. | 
 | If swallowed | Rinse mouth with water. Obtain medical examination and treatment without delay. | 

## Slide 68: Class II Specified Chemical Substances
Ethyleneimine (CH₂–CH₂)NH CAS RN:151-56-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders, Liver disorders, Kidney disorders, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Dermatitis, Pruritus(Itching), Skin redness, Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, drowsiness, Vomiting, General fatigue, Cough, Sputum, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Weight loss | 
Handling Precautions | ・Keep away from heat, hot surfaces, sparks, open flame and other ignition sources. ・Keep container tightly closed; store in a cool place. ・Take measures to prevent static‐electricity discharge. ・Do not inhale dust or vapor. ・Avoid contact with eyes, skin and clothing. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated location. ・Prevent release to the environment. ・Wear appropriate respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Organic–gas cartridge respirator with dust filter(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the affected person to fresh air and have them rest in a position that eases breathing. ・Call a physician immediately. ・Keep them in a semi-recumbent position. ・Artificial respiration may be required. | 
 | If on skin | ・Immediately remove all contaminated clothing. Wash the affected skin with water(or shower). ・Call a physician immediately. | 
 | If in eyes | ・Rinse cautiously with water for several minutes, removing contact lenses if easy to do. Continue rinsing. ・Call a physician immediately. | 
 | If swallowed | ・Call a physician immediately. ・Rinse mouth; do not induce vomiting. ・If conscious, give 1–2 cups of water. | 

## Slide 69: Class II Specified Chemical Substances
Ethylene oxide (CH₂–CH₂)O CAS RN:75-21-8 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system disorders, Peripheral neuropathy, Respiratory tract disorders, Pulmonary disorders, Kidney disorders, Hematologic disorders, Carcinogenicity, Reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus, Skin erythema, Eczema, Urticaria, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Paresthesia and motor dysfunction of the limbs, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Respiratory distress, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Unsteadiness, Weight loss | 
Handling Precautions | ・Keep away from heat, hot surfaces, sparks, open flame and other ignition sources. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated location. ・Do not inhale dust or vapor. ・Do not remove contaminated work clothing from the workplace. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Use an ethylene-oxide-rated gas mask.(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・If the person is unconscious but breathing, place them in the recovery (lateral) position and protect against hypothermia. ・If feeling unwell or experience any respiratory symptoms, seek medical attention. ・If breathing difficulty occurs, administer oxygen. ・If breathing stops, perform artificial respiration with a resuscitation bag or by mouth-to-nose/mouth method(only in emergencies). ・Be aware that symptoms may be delayed. ・Move to fresh air and keep in a comfortable position. ・Seek medical attention immediately. | 
 | If on skin | ・Protect yourself and remove the victim from the source of exposure. ・Immediately flush affected skin with water or shower for at least 20 minutes. ・Lay the victim in a warm, quiet place to prevent hypothermia. ・Remove all contaminated clothing without delay. | 
 | If in eyes | ・Hold eyelids open and rinse with running water for at least 10 minutes, removing contact lenses if easily done. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth and have the victim spit out any liquid. ・If conscious, give 1–2 cups of water to drink. ・Do not induce vomiting. ・If vomiting occurs naturally, position the head lower than the chest and lie prone to prevent aspiration. ・Do not give anything further by mouth. ・Be aware that symptoms may be delayed. | 

## Slide 70: Class II Specified Chemical Substances
Vinyl chloride C2H3Cl CAS RN:75-01-4 |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Central nervous system disorders, Respiratory disorders, Liver disorders(including portal hypertension), Hepatic angiosarcoma, Hepatocellular carcinoma, Cardiovascular disorders(e.g. Raynaud’s phenomenon), Testicular disorders, Hematologic disorders, Phalangeal bone resorption, Suspected reproductive toxicity | 
 | Symptoms | Dermatitis, Pruritus(Itching), Skin erythema, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Easy fatigability, Jaundice, Facial pallor, Palpitations, Dizziness, Unsteady gait, Finger pain, Raynaud’s‐type symptoms, Weight loss | 
Handling Precautions | ・Keep away from heat, hot surfaces, sparks, open flame and other ignition sources. ・Do not inhale dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated location. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air. ・If breathing difficulty occurs, administer oxygen. If respiration ceases, perform artificial respiration. ・Obtain immediate medical attention. | 
 | If on skin | ・Remove contaminated clothing and rinse the entire body under a shower. ・If skin has frozen (in case of very cold exposure), thaw with lukewarm water, remove clothing carefully, rinse repeatedly, and cover the affected area with a sterile dressing. ・Obtain medical attention. | 
 | If in eyes | ・Rinse continuously with water or sterile saline for 20–30 minutes; remove contact lenses if easily done. ・Obtain immediate medical attention. | 
 | If swallowed | Ingestion is highly unlikely (the substance vaporizes rapidly). | 

## Slide 71: Class II Specified Chemical Substances
Chlorine Cl2 CAS RN:7782-50-5 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Liver disorders, Kidney disorders, Hematologic disorders, Respiratory tract disorders (including pulmonary injury), Dental disorders(tooth erosion) | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus, Skin erythema, Skin lesions, Corneal abnormalities, Visual impairment, Cough, Sputum, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Respiratory distress, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Oral pain, Toothache | 
Handling Precautions | ・Keep away from clothing and other combustible materials. ・Do not use grease or oil on valves and fittings. ・Do not inhale dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated location. ・Avoid release to the environment. ・If ventilation is inadequate, wear appropriate respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Use a halogen-gas-rated respirator.(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the person to fresh air and keep them in a comfortable breathing position. ・Call a physician immediately. ・If feeling unwell, seek medical attention. ・If symptoms of respiratory distress appear, seek medical attention at once. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Call a physician immediately. ・Rinse the affected skin thoroughly with water or shower. ・If feeling unwell, seek medical attention. ・Wash and launder contaminated clothing before re-use. | 
 | If in eyes | ・Call a physician immediately. ・Rinse cautiously with water for several minutes, removing contact lenses if easy to do; continue rinsing. ・Seek medical attention if irritation persists. | 
 | If swallowed | ・Call a physician immediately. ・Rinse mouth; do not induce vomiting. ・Seek medical attention if any discomfort develops. | 

## Slide 72: Class II Specified Chemical Substances
Auramine [(CH₃)₂N–C₆H₄–CH=N–C₆H₄–N(CH₃)₂]⁺ Cl⁻ CAS RN:492-80-8,2465-27-2,etc. |  |  | 
Health Hazards | Possible Diseases | Liver disorders, Urinary system disorders, Urinary-tract tumors | 
 | Symptoms | General fatigue, Easy fatigability, Jaundice, Hematuria, Frequent urination, Painful urination, Lower abdominal pain, Sensation of residual urine, Weight loss | 
Handling Precautions | ・Avoid inhaling dust or vapor. ・Do not eat, drink or smoke in the work area. ・Keep containers tightly closed. ・Wash hands thoroughly after handling. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Organic–gas cartridge respirator with dust filter(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Lay the victim in a quiet place and protect against hypothermia. ・Move to fresh air and keep them resting in a comfortable position. ・If feeling unwell or respiratory symptoms develop, seek medical attention. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Rinse affected skin under running water or shower, then wash thoroughly with soap and water. | 
 | If in eyes | ・Spread the eyelids and flush with water for at least 10 minutes. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・Contact a physician immediately. ・If the person is conscious, give 1–2 cups of water to drink. | 

## Slide 73: Class II Specified Chemical Substances
o-Toluidine CH₃–C₆H₄–NH₂ CAS RN:95-53-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Hematologic disorders(hemolytic anemia or methemoglobinemia), Urinary-tract disorders, Urinary-tract tumors(e.g. bladder cancer) | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Hematuria, Frequent urination, Painful urination, Lower abdominal pain, Sensation of residual urine, Facial pallor, Palpitations, Unsteadiness, Cyanosis, Discolored urine, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flames and other ignition sources. ・Do not inhale dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated location. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and have them rest in a position that eases breathing. ・Artificial respiration may be required. ・Contact medical services immediately for diagnosis and treatment. ・Special medical procedures may be necessary. | 
 | If on skin | ・Remove contaminated clothing. Rinse the skin under running water, then wash thoroughly with soap and water. ・Seek immediate medical attention and special treatment. ・Special medical procedures may be necessary. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy, then continue rinsing. ・Obtain immediate medical attention and special treatment as required. | 
 | If swallowed | ・Rinse mouth. ・Contact medical services immediately for diagnosis and treatment. ・Special medical procedures may be necessary. | 

## Slide 74: Class II Specified Chemical Substances
o-Phthalodinitrile NC–C₆H₄–CN CAS RN:91-15-6 |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders, Testicular disorders, Ocular disorders | 
 | Symptoms | Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Seizures with loss of consciousness, Memory impairment, Insomnia, Nausea, Loss of appetite, Facial pallor, Fine tremor of the fingers, Cranial-nerve symptoms, Blurred vision, Photophobia, Gastrointestinal symptoms(abdominal pain, diarrhea, vomiting, etc.), Weight loss | 
Handling Precautions | ・Do not inhale dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Keep containers tightly closed. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Organic–gas cartridge respirator with dust filter(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | If feeling unwell, seek medical attention. | 
 | If on skin | ・Wash affected area with water and soap. ・If skin irritation occurs, obtain medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Seek medical attention immediately. ・ Rinse mouth. | 

## Slide 75: Class II Specified Chemical Substances
Cadmium and its compounds Cd CAS RN:7440-43-9,10022-68-1,10108-64-2,10124-36-4,10325-94-7,etc. |  |  | 
Health Hazards | Possible Diseases | Airway disorders, Pulmonary disorders, Kidney disorders, Gastrointestinal disorders, Hematologic disorders, Osteomalacia (bone softening), Carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Cough, Sputum, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Dyspnea(difficulty breathing), Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations (Heart racing), Dizziness, Unsteadiness, Abdominal pain, Diarrhea, Vomiting, Loss of appetite, General fatigue, Weight loss | 
Handling Precautions (カドミウム) | ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Avoid inhaling dust or vapor. ・Use only outdoors or in a well-ventilated location. ・If ventilation is inadequate, wear appropriate respiratory protection. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex 〇, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (カドミウム) | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・If they feel unwell, call a physician. | 
 | If on skin | ・Rinse the affected skin promptly with water. ・If they feel unwell, call a physician. ・Remove and launder contaminated clothing before reuse. ・Continue rinsing skin with water for several minutes. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | Rinse mouth immediately. Seek medical evaluation promptly. | 

## Slide 76: Class II Specified Chemical Substances
Chromic acid and its salts CrO3 CAS RN:1333-82-0,7789-00-6,13517-17-4,13530-65-9,7775-11-3,etc. |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders(e.g. ulceration), Skin sensitization, Airway disorders, Pulmonary disorders, Respiratory sensitization, Respiratory-tract tumors(lung or upper airway cancer), Nasal abnormalities(septal perforation), Olfactory dysfunction, Liver disorders, Kidney disorders, Cardiovascular disorders, Hematologic disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Skin pain, Skin ulceration, Eczema, Urticaria, Nasal-mucosa lesions, Septal perforation, Cough, Sputum, Shortness of breath, Asthma-like symptoms, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Dyspnea, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Dizziness, Unsteadiness, Weight loss | 
Handling Precautions (Chromic anhydride) | ・Keep away from heat, sparks, open flame and high-temperature sources. ・Keep away from clothing and other combustible materials. ・Avoid mixing with combustible substances. ・Do not inhale dust, fume or vapor. ・Avoid contact with eyes, skin and clothing. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated location. ・Do not remove contaminated clothing from the work area. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex △, Chloroprene △, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Chromic anhydride) | If inhaled | ・Move the victim to fresh air and have them rest in a position that eases breathing. ・Call a physician immediately. ・If breathing is difficult, repeat fresh-air/rest steps and seek urgent medical care. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Rinse affected skin under running water or shower, then wash thoroughly with soap and water. ・Launder contaminated clothing before reuse. ・Call a physician without delay. ・If irritation or rash occurs, obtain medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy, then continue rinsing. ・Call a physician immediately. | 
 | If swallowed | ・Rinse mouth; do not induce vomiting.・Call a physician immediately. | 

## Slide 77: Class II Specified Chemical Substances
Chloromethyl methyl ether CH₃–O–CH₂Cl CAS RN:107-30-2 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Airway and pulmonary disorders, Respiratory-tract tumors | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching, skin redness, Cough, Sputum, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Difficulty breathing, General fatigue, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flames and other ignition sources. ・Keep container tightly closed. ・Take measures to prevent static‐electric discharge. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Do not inhale dust or vapor. ・Use only outdoors or in a well-ventilated location. ・Wear appropriate respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Organic–gas cartridge respirator with dust filter(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the person to fresh air and have them rest in a position that eases breathing. ・Call a physician immediately. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Rinse skin thoroughly under running water or in a safety shower. ・Wash contaminated clothing before reuse. ・Call a physician immediately. | 
 | If in eyes | ・Call a physician immediately. ・Rinse eyes cautiously with water for several minutes. Remove contact lenses if easy, then continue rinsing. | 
 | If swallowed | ・Rinse mouth; do not induce vomiting. ・Call a physician immediately. | 

## Slide 78: Class II Specified Chemical Substances
Divanadium pentaoxide V2O5 CAS RN:1314-62-1 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Airway and pulmonary disorders, Liver disorders, Kidney disorders, Carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus(Itching), Skin redness, Skin pallor, Tongue discoloration(greenish), Hyperkeratosis of the palmar fingertips, Finger tremor, Cough, Sputum, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Difficulty breathing, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Weight loss | 
Handling Precautions | ・Do not inhale dust or vapour. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated location. ・Avoid release to the environment. ・If ventilation is inadequate, wear appropriate respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. ・Emergency medical treatment may be required. ・Seek medical attention immediately. | 
 | If on skin | ・Rinse the affected skin promptly with water. ・Obtain medical attention. ・Wash or discard contaminated clothing before reuse. | 
 | If in eyes | Rinse cautiously with water for several minutes. Remove contact lenses if easy, then continue rinsing. | 
 | If swallowed | ・Seek medical attention immediately. ・Emergency medical treatment may be required. ・Rinse mouth. | 

## Slide 79: Class II Specified Chemical Substances
Cobalt and its inorganic compounds Co CAS RN:7440-48-4,1307-96-6,10026-24-1,10124-43-3,7646-79-9,etc. |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Airway disorders, Pulmonary disorders, Respiratory sensitization, Cardiovascular disorders, Endocrine disorders(thyroid), Hematologic disorders, Reproductive disorders(male), Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Dermatitis, Pruritus(Itching), Skin redness, Eczema, Urticaria, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Asthma-like attacks, Runny nose, Nasal congestion, Nasal/throat pain, Bradycardia, Edema, Chest pain, Dyspnea, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Weight loss | 
Handling Precautions (Cobalt) | ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Avoid inhalation of dust or vapor. ・Use only outdoors or in a well-ventilated location. ・If ventilation is inadequate, wear respiratory protection. ・Do not remove contaminated work clothing from the work area. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Cobalt) | If inhaled | ・If respiratory symptoms appear, call a physician. ・Move the person to fresh air and have them rest in a position that eases breathing. ・If unconscious but breathing, place in a stable side-lying position and protect from hypothermia. ・If feeling unwell or if respiratory symptoms persist, seek medical attention. ・If airway or respiratory irritation occurs, administer an inhaled glucocorticoid spray as soon as possible. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Rinse affected skin under running water or safety shower, then wash thoroughly with soap and water. ・If irritation or rash develops, obtain medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy, then continue rinsing. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth and spit out. ・Call a physician immediately. ・If conscious, give 1–2 cups of water. ・If spontaneous vomiting occurs, prevent aspiration by lowering the head below chest level and placing the person prone. | 

## Slide 80: Class II Specified Chemical Substances
Coal tar Chemical formula：not specified CAS RN:8007-45-2 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Gastrointestinal disorders, Hematologic disorders, Airway disorders, Pulmonary disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Acne-like eruptions, Hyperpigmentation, Warts, Skin ulcers, Gas-patch lesions, Eczema, Urticaria, Cough, Sputum, shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Respiratory difficulty, Facial pallor, Palpitations, Dizziness, Unsteadiness, General fatigue, Easy fatigability, Weight loss, Abdominal pain, Diarrhea, Vomiting, Loss of appetite | 
Handling Precautions | ・Wash hands thoroughly after handling. ・Avoid inhaling dust or vapor. ・Use only outdoors or in a well-ventilated area. ・Do not eat, drink or smoke in the work area. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ×, Chloroprene 〇, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・Seek medical attention. | 
 | If on skin | ・Remove contaminated clothing and shoes immediately. ・Rinse affected skin with plenty of water or soapy water, then continue flushing under running water for at least 15 minutes. ・If hot (molten) coal tar contacts skin, cool immediately with copious water to prevent burn progression. | 
 | If in eyes | ・Rinse eyes cautiously with water for several minutes. Remove contact lenses if easy, then continue rinsing. ・Seek medical attention. | 
 | If swallowed | If feeling unwell after swallowing, seek medical attention. | 

## Slide 81: Class II Specified Chemical Substances
Propylene Oxide (CH₃–CH–CH₂)O CAS RN:75-56-9 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system disorders, Airway disorders, Pulmonary disorders, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Eczema, Urticaria, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Respiratory difficulty, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Keep container tightly closed. ・Take precautions against static‐electric discharge. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Avoid inhaling dust or vapor. ・Use only outdoors or in a well-ventilated area. ・Do not remove contaminated work clothing from the work area. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Organic vapor respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・If feeling unwell, seek medical attention. ・Move to fresh air and rest in a comfortable breathing position. | 
 | If on skin | ・Rinse skin thoroughly with water or shower. ・If irritation occurs, seek medical attention. ・Remove and launder contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, seek medical attention. | 

## Slide 82: Class II Specified Chemical Substances
Antimony trioxide Sb2O3 CAS RN:1309-64-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders(e.g. antimony rash), Airway disorders, Pulmonary disorders, Myocardial disorders, Gastrointestinal disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis(antimony rash), Itching, Skin redness, Headache, Dizziness, Vomiting, Cough, Sputum, Shortness of breath, Nasal/throat pain, Chest pain, Respiratory difficulty, Abdominal pain, Diarrhea, Loss of appetite, General fatigue, Weight loss | 
Handling Precautions | ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Avoid inhaling dust or vapor. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move to fresh air and rest in a comfortable breathing position. ・Call a physician. ・If unconscious but breathing, place in a stable side-lying position and protect from hypothermia. ・ If feeling unwell or if respiratory irritation occurs, seek medical attention. ・If airway/respiratory irritation persists, administer an inhaled glucocorticoid spray as soon as possible. | 
 | If on skin | ・Rinse affected skin under running water or safety shower, then wash thoroughly with soap and water. ・If irritation or rash develops, seek medical attention. ・Remove all contaminated clothing immediately. | 
 | If in eyes | ・If symptoms persist, seek medical attention. ・Rinse cautiously with water for at least 10 minutes, holding eyelids open. Remove contact lenses if easy to do, then continue rinsing. | 
 | If swallowed | ・Rinse mouth. ・Call a physician immediately. ・If conscious, give 1–2 cups of water. ・If spontaneous vomiting occurs, lower the head below chest level and place the person prone to prevent aspiration. | 

## Slide 83: Class II Specified Chemical Substances
Potassium cyanide KCN CAS RN:151-50-8 |  |  | 
Health Hazards | Possible Diseases | Ocular disorders, Skin disorders, Central nervous system disorders, Respiratory distress, Respiratory arrest, Loss of consciousness, Convulsions, Liver disorders, Kidney disorders, Gastrointestinal disorders, Endocrine disorders(thyroid) | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Altered taste sensation, Palpitations, Hoarseness of voice, Pupil dilation, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Loss of consciousness, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Dyspnea, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Abdominal pain, Diarrhea, Loss of appetite, Weight loss | 
Handling Precautions | ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Avoid contact with eyes, skin or clothing. ・Avoid inhaling dust or vapor. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex 〇, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | A gas-mask respirator for hydrogen cyanide with particulate-filter function.(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・While protecting yourself, evacuate the victim from the danger area to fresh air. ・If unconscious but breathing, place in a stable side-lying position and protect from hypothermia. ・Call a physician. ・Position the victim semi-sitting if possible. ・If breathing has stopped, perform artificial respiration using a resuscitation bag or mouth-nose technique (mouth-to-mouth only in emergencies). ・If breathing is difficult, administer oxygen. ・If any respiratory symptoms or general malaise occur, seek medical attention. | 
 | If on skin | ・Wear protective gloves when performing first aid. ・Immediately remove all contaminated clothing. ・Call a physician. ・Rinse affected skin under running water or shower for at least 20 minutes. ・Lay the victim in a quiet place and prevent hypothermia. | 
 | If in eyes | ・Protect the unaffected eye, hold the eyelids open and flush the affected eye with gentle running water for at least 10 minutes. ・Note: Contact with KCN dust or solution can be life-threatening. Seek urgent medical care. | 
 | If swallowed | ・Call a physician immediately. ・If conscious, give 1–2 glasses of water. ・Always wear protective gloves when providing care. ・If respiratory arrest occurs, do not perform mouth-to-mouth; supply oxygen via a non-rebreather or oxygen mask. ・If spontaneous vomiting occurs, position the head below chest level and prone to prevent aspiration. | 

## Slide 84: Class II Specified Chemical Substances
Hydrogen cyanide HCN CAS RN:74-90-8 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Cardiovascular system disorders, Gastrointestinal system disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Altered taste sensation, Palpitations(tachycardia), Hoarseness of voice, Respiratory difficulty, Pupil dilation(mydriasis), Flushing of skin or mucous membranes, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Abdominal pain, Diarrhea, Loss of appetite, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks and open flames. ・Take precautions against static‐electric discharge. ・Wear appropriate respiratory protection. ・Avoid contact with eyes, skin or clothing. ・Do not inhale dust or vapors. ・Do not eat, drink or smoke in the work area. ・Wash hands thoroughly after handling. ・Use only outdoors or in a well-ventilated area. ・Keep container tightly closed. ・Avoid release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Hydrogen cyanide gas-mask respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Remove the victim to fresh air and allow to rest in a comfortable breathing position. ・Call a physician immediately. ・If the person feels unwell, seek medical attention. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Call a physician. ・Rinse affected skin quickly under running water. ・Wash thoroughly with plenty of water and soap. ・If feeling unwell, seek medical attention. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes, holding eyelids open. Remove contact lenses if easy to do, then continue rinsing. ・If eye irritation persists or if feeling unwell, seek medical attention. | 
 | If swallowed | ・Call a physician immediately. ・Rinse mouth. ・If feeling unwell, seek medical attention. | 

## Slide 85: Class II Specified Chemical Substances
Sodium cyanide NaCN CAS RN:143-33-9S |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Kidney disorders, Gastrointestinal disorders, Endocrine system disorders(adrenal), Testicular disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Disturbance of taste, Palpitations, Hoarseness of voice, Respiratory distress, Pupil dilation, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Hematuria, Polyuria, Oliguria, Edema, Abdominal pain, Diarrhea, Loss of appetite, Weight loss | 
Handling Precautions | ・Do not eat, drink or smoke in the work area. ・Use personal protective equipment and local exhaust or general ventilation to avoid exposure. ・Avoid contact with eyes, skin or clothing. ・Do not inhale dust. ・Wash hands thoroughly after handling. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex 〇, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Hydrogen cyanide gas‐mask respirator with particulate‐filter function (Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and allow to rest in a comfortable breathing position. ・Seek medical attention. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Seek medical attention immediately. ・Rinse affected skin thoroughly with plenty of water and soap. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes, holding eyelids open. Remove contact lenses if easy to do, then continue rinsing. ・If irritation persists or victim feels unwell, seek medical attention. | 
 | If swallowed | ・Seek medical attention immediately. ・Rinse mouth. | 

## Slide 86: Class II Specified Chemical Substances
3,3'-Dichloro-4,4'-diaminodiphenylmethane NH₂‑C₆H₃(Cl)‑CH₂‑C₆H₃(Cl)‑NH₂ CAS RN:101-14-4 |  |  | 
Health Hazards | Possible Diseases | Liver disorders, Kidney disorders, Gastrointestinal disorders, Blood disorders, Urinary‐tract tumors, Respiratory‐tract tumors | 
 | Symptoms | Cough, Sputum, Chest pain, Dyspnea, Upper abdominal discomfort, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Abdominal pain, Diarrhea, Vomiting, Loss of appetite, Facial pallor, Palpitations, Dizziness, Unsteadiness, Weight loss | 
Handling Precautions | ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Organic-gas respirator with particulate-filter function (Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and allow them to rest in a comfortable breathing position. ・Seek medical attention. | 
 | If on skin | ・Remove contaminated clothing. ・Rinse skin, then wash thoroughly with water and soap. | 
 | If in eyes | Flush the eye with plenty of water.(Remove contact lenses if easy to do, then continue rinsing.) | 
 | If swallowed | ・Rinse mouth. ・Seek medical attention. | 

## Slide 87: Class II Specified Chemical Substances
Dimethyl 2,2-dichlorovinyl phosphate (CH₃O)₂P(=O)OCH=CCl₂ CAS RN:62-73-7 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system disorders, Peripheral nervous system disorders, Organophosphate poisoning, Liver disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Eczema, Urticaria, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Paresthesia and motor disturbances of the limbs, Pupil constriction(miosis), Excessive salivation, Nausea, Diarrhea, Easy fatigability, Jaundice, Weight loss | 
Handling Precautions | ・Do not inhale dust or vapors. ・Avoid contact with eyes, skin or clothing. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated area. ・Do not remove contaminated work clothes from the workplace. ・Prevent release to the environment. ・If ventilation is inadequate, wear respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex: no data, Chloroprene: no data, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Organic-gas respirator with particulate-filter function (Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and allow to rest in a comfortable breathing position. ・Call a physician immediately. ・Special emergency treatment may be required. | 
 | If on skin | ・Wash the affected area with plenty of water and soap. ・Call a physician immediately. ・special treatment may be required. ・If irritation or rash develops, seek medical attention. ・Remove contaminated clothing at once and launder before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes, holding the eyelids open. Remove contact lenses if easy to do, then continue rinsing. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Call a physician immediately. ・Special treatment may be required. ・Rinse mouth thoroughly. | 

## Slide 88: Class II Specified Chemical Substances
1,1-Dimethylhydrazine (CH₃)₂N–NH₂ CAS RN:57-14-7 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system disorders, Airway disorders, Pulmonary disorders, Liver disorders, Blood disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Eczema, Urticaria, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, General fatigue, Easy fatigability, Jaundice, Facial pallor, Palpitations, Dizziness, Unsteadiness, Chest pain, Dyspnea, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flame and other ignition sources. ・Keep container tightly closed. ・Take measures against static‐electric discharge. ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated area. ・Do not remove contaminated work clothes from the work area. ・Avoid release to the environment. ・If ventilation is inadequate, wear appropriate respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Ammonia-rated gas mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move victim to fresh air and allow to rest in a comfortable breathing position. ・Call a physician immediately for examination and treatment. ・Special emergency measures may be required. | 
 | If on skin | ・Rinse the affected area with plenty of water and soap. ・Immediately remove all contaminated clothing. ・If feeling unwell or if irritation persists, seek medical attention. ・Special treatment may be needed. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes, holding eyelids open. Remove contact lenses if easy to do, then continue rinsing. ・If eye irritation continues, seek medical attention. | 
 | If swallowed | ・Call a physician immediately. ・Special treatment may be needed. ・Rinse mouth thoroughly. | 

## Slide 89: Class II Specified Chemical Substances
Methyl bromide CH3Br CAS RN:74-83-9 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders (ataxia, tremors, etc.), Mental disorders (personality changes, delirium, hallucinations, etc.), Airway and pulmonary disorders, Cardiovascular disorders, Liver disorders, Kidney disorders, Gastrointestinal disorders, Hematopoietic disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Hallucinations or altered consciousness, Rhinitis, Sore throat, Cough, Limb numbness, Reduced visual acuity, Memory loss, Speech disturbances, Hyperreflexia, Gait difficulty, Headache, Head heaviness, Dizziness, Nausea, Vomiting, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Abdominal pain, Diarrhea, Loss of appetite, Facial pallor, Palpitations, Lightheadedness, Chest pain, Shortness of breath | 
Handling Precautions | ・Keep away from heat, sparks, open flames and other ignition sources. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated area. ・Avoid inhaling dust or vapors. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Methyl bromide gas-mask respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the casualty to fresh air. ・If breathing is difficult, administer oxygen. Have the patient take repeated deep breaths using an inhaled glucocorticoid spray as soon as possible. ・If breathing stops, perform mouth-to-nose or mouth-to-mouth resuscitation. ・Seek immediate medical attention. | 
 | If on skin | ・Remove contaminated clothing without delay. ・Rinse the affected skin with plenty of water for at least 10–20 minutes. 5% sodium bicarbonate solution is optimal. ・In case of frostbite, rinse with large amounts of water but do not remove clothing. ・Seek immediate medical attention. | 
 | If in eyes | ・Rinse eyes with large volumes of water for at least 10 minutes, removing contact lenses if easily done. Continue rinsing. ・After exposure to cryogenic liquid, flush briefly without forcing eyelids open. ・Seek medical attention. | 
 | If swallowed | ・Oral ingestion is unlikely due to the substance’s low boiling point. ・If ingested, rinse the mouth and give small sips of water. Do not administer vegetable oil, castor oil, milk or alcohol. ・Seek immediate medical attention. | 

## Slide 90: Class II Specified Chemical Substances
Dichromic acid and its salts H2Cr2O7 CAS RN:13530-68-2,10588-01-9,7789-09-5,7778-50-9,7789-12-0,etc. |  |  | 
Health Hazards | Possible Diseases | Skin disorders(e.g. ulceration), Airway disorders, Pulmonary disorders, Skin sensitization, Respiratory sensitization, Respiratory tract tumors(lung or upper airway cancer), Nasal abnormalities(e.g. septal perforation), Liver disorders, Kidney disorders | 
 | Symptoms | Dermatitis, Itching, Skin redness, Skin pain, Ulceration, Eczema, Urticaria, Chest pain, Nasal mucosal changes, Nasal septal perforation, Cough, Sputum, Shortness of breath, Chest tightness, Nasal/throat pain, Asthma-like attacks, General fatigue, Easy fatigability, Jaundice, hematuria, Polyuria, Oliguria, Edema, Dyspnea, Weight loss | 
Handling Precautions (Dichromic acid) | ・Do not eat, drink or smoke in the work area. ・Wash hands thoroughly after handling. ・Avoid inhaling mists, fumes, vapors or sprays. ・If ventilation is inadequate, wear appropriate respiratory protection. ・Do not remove contaminated work clothes from the workplace. ・Prevent release into the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】(Dichromic acid) Nitrile ×, Latex △, Chloroprene △, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Dust/acid-gas combination respirator or cartridge for acidic gases(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Dichromic acid) | If inhaled | ・Call a physician immediately. ・If breathing is difficult, move the victim to fresh air and allow them to rest in a comfortable breathing position. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Flush the affected skin with plenty of water or shower. ・Launder contaminated clothing before reuse. ・If irritation or rash develops, seek medical attention. ・Wash thoroughly with soap and water. ・Contact a physician immediately. | 
 | If in eyes | ・Rinse cautiously with water for several minutes, holding eyelids open. Remove contact lenses if easy to do, then continue rinsing. ・Call a physician immediately. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth. Do not induce vomiting. ・Call a physician immediately. | 

## Slide 91: Class II Specified Chemical Substances
Mercury and its inorganic compounds Hg CAS RN:7439-97-6,7546-30-7、7487-94-7,10045-94-0,10112-91-1,etc. |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system disorders(tremors, gait disturbance, etc.), Restlessness, Memory loss, Insomnia and other psychiatric disorders, Oral mucosal disorders, Peripheral neuropathy, Liver disorders, Kidney disorders, Blood disorders, Cardiovascular disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Eczema, Urticaria, Hand tremors, Headache, Head heaviness, Dizziness, Nausea, Vomiting, General fatigue, Easy fatigability, Insomnia, Jaundice, Paresthesia and motor disturbances of the limbs, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Unsteadiness, Pain of the oral mucosa, Toothache | 
Handling Precautions (Mercury) | ・Avoid inhaling dust, fumes, gases, mists or vapors. ・Wash hands and exposed skin thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated area. ・Do not remove contaminated work clothing from the workplace. ・Avoid release to the environment. ・Wear appropriate respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex 〇, Chloroprene 〇, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Mercury-rated gas mask (Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Mercury) | If inhaled | ・Move the victim to fresh air and allow them to rest in a comfortable breathing position. ・Provide artificial respiration if breathing has stopped. ・Call a physician immediately. ・Special emergency measures may be required. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Rinse the affected skin area with plenty of water, then wash thoroughly with soap. ・Seek medical attention. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easily done, then continue rinsing. ・Seek medical attention. | 
 | If swallowed | ・Call a physician immediately for examination and treatment. ・Rinse mouth. | 

## Slide 92: Class II Specified Chemical Substances
Tolylene diisocyanate O=C=N–C₆H₃–CH₃–N=C=O CAS RN:26471-62-5,584-84-9,91-08-7,etc |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Airway disorders, Pulmonary disorders, Respiratory sensitization, Visual disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Eczema, Urticaria, Throat irritation, Visual disturbances, Cough, Sputum, Chest tightness, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Dyspnea, Asthma-like attacks, General fatigue, Weight loss | 
Handling Precautions | ・Do not eat, drink or smoke in the work area. ・Use personal protective equipment and ventilation to avoid exposure. ・Use only outdoors or in a well-ventilated area. ・Avoid inhalation of dust. ・Wash hands thoroughly after handling. ・Do not remove contaminated work clothing from the workplace. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene △, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Organic-gas respirator equipped with particulate-filter function(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and allow them to rest in a comfortable breathing position. ・Call a physician immediately. ・Seek medical attention. | 
 | If on skin | ・Remove all contaminated clothing at once. ・Call a physician immediately. ・Rinse affected skin with plenty of water or shower. ・Seek medical attention. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Call a physician immediately. ・Rinse eyes cautiously with water for several minutes, removing contact lenses if easily done, then continue rinsing. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Call a physician immediately. ・Rinse mouth; do not induce vomiting. ・Seek medical attention. | 

## Slide 93: Class II Specified Chemical Substances
Naphthalene C10H8 CAS RN:91-20-3 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system disorders, Ocular toxicity(cataracts, retinal abnormalities), Airway disorders, Digestive system disorders, Blood disorders(hemolytic anemia), Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Eczema, Urticaria, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Blurred vision, Photophobia, Decreased visual acuity, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Cyanosis, Abdominal pain, Diarrhea, Loss of appetite, Weight loss, Facial pallor, Rapid heartbeat, Unsteadiness | 
Handling Precautions | ・Keep away from heat, high temperatures, sparks, open flames and other ignition sources. ・Ground and bond containers during transfer. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in work areas. ・Do not remove contaminated work clothes from the workplace. ・Avoid inhaling dusts or vapors. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage
 | Type of respiratory protection |  | Organic-gas respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air. ・If breathing is difficult, administer oxygen. ・If breathing stops, perform mouth-to-nose, or if not possible, mouth-to-mouth resuscitation. ・Seek medical attention immediately. | 
 | If on skin | ・Remove contaminated clothing at once. ・Rinse the affected skin thoroughly with water and soap. Then rinse alternately with polyethylene glycol 400 and water for several minutes, finally wash again with soap and water. ・Seek medical attention. | 
 | If in eyes | ・Rinse eyes under running water for at least 10 minutes. Remove contact lenses if easy to do, then continue rinsing. ・Seek medical attention. | 
 | If swallowed | ・Rinse mouth. Do not induce vomiting. Do not administer edible oils, castor oil, milk or alcohol. ・Seek medical attention immediately. | 

## Slide 94: Class II Specified Chemical Substances
Nickel compounds Ni CAS RN:10101-97-0,13478-00-7,7718-54-9,7791-20-0,1313-99-1,etc. |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Skin sensitization, Airway disorders, Respiratory sensitization, Kidney disorders, Respiratory system tumors(lung cancer or upper respiratory tract cancer), Nasal abnormalities (rhinitis, sinusitis, nasal septum perforation, etc.) | 
 | Symptoms | Dermatitis, Itching, Skin redness, Eczema, Urticaria, Rhinitis, Pain around the cheeks, nose and forehead, Facial or eyelid swelling, Fever, Head heaviness, Loss of smell, Nasal septum perforation, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, General fatigue, Hematuria, Polyuria, Oliguria, Edema, Asthma-like attacks, Weight loss | 
Handling Precautions (Nickel(II) Sulfate Hexahydrate) | ・Avoid inhaling dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in work areas. ・Do not remove contaminated work clothing from the workplace. ・If ventilation is inadequate, wear respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】(Nickel(II) Sulfate Hexahydrate) Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Nickel(II) Sulfate Hexahydrate) | If inhaled | ・If breathing is difficult, move to fresh air and rest in a comfortable position. ・If respiratory symptoms occur, seek medical attention. ・ If feeling unwell, have the victim examined and treated by a physician. | 
 | If on skin | ・Wash affected area thoroughly with plenty of water and soap. ・Launder contaminated clothing before reuse. ・If irritation or rash develops, seek medical attention. | 
 | If in eyes | ・Rinse eyes with water for several minutes, holding eyelids open. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, seek medical attention. | 

## Slide 95: Class II Specified Chemical Substances
Nickel carbonyl Ni(CO)4 CAS RN:13463-39-3 |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Skin sensitization, Central nervous system disorders, Airway disorders, Pulmonary disorders, Respiratory sensitization, Liver disorders, Kidney disorders, Digestive system disorders, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Dermatitis, Pruritus, Erythema(redness), Eczema, Urticaria(hives), Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Hematuria, Polyuria, Oliguria, Edema, Cough, Shortness of breath, Runny nose, Nasal congestion, nasal/throat pain, Chest pain, Asthma-like attacks, Weight loss | 
Handling Precautions | ・Do not eat, drink or smoke in work areas. ・Keep away from heat, sparks, open flames and hot surfaces. ・Prevent ignition by static discharge or sparks. ・Use appropriate personal protective equipment and ensure adequate ventilation (e.g. local exhaust). ・Use only outdoors or in well-ventilated areas. ・Avoid inhalation of dusts or vapors. ・Wash hands thoroughly after handling. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Supplied-air respirator (Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and allow them to rest in a comfortable position for breathing. ・Call a physician immediately and obtain medical treatment. | 
 | If on skin | ・Remove contaminated clothing at once. ・Rinse the affected skin area promptly with water, then wash thoroughly with soap and water. ・If irritation develops, seek medical attention. ・Obtain medical treatment. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Call a physician immediately. ・Rinse eyes with water for several minutes, removing contact lenses if easy to do; continue rinsing. ・Obtain medical treatment. | 
 | If swallowed | ・Rinse mouth. ・Obtain medical treatment. | 

## Slide 96: Class II Specified Chemical Substances
Nitroglycol O₂NO–CH₂–CH₂–ONO₂ CAS RN:628-96-6 |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders, Peripheral neuropathy, Cardiovascular disorders(angina‐like attacks or vasomotor nerve dysfunction), Hematologic disorders, Digestive system disorders | 
 | Symptoms | Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Stiff shoulders, Feeling of cold, Neuralgia, Weakness, Abdominal pain, Diarrhea, Nausea, Loss of appetite, Sensory disturbances of the limbs, Motor dysfunction of the limbs, Facial pallor, Palpitations(tachycardia), Unsteadiness | 
Handling Precautions | ・Do not handle roughly (avoid crushing, impact or friction). ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in work areas. ・Avoid inhaling dusts or vapors. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Organic-gas respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and have them rest in a comfortable position. ・Call a physician immediately. ・If the victim is unconscious but breathing, place them on their side in a stable position and protect from hypothermia. ・If feeling unwell or respiratory symptoms develop, seek medical attention. ・If breathing is difficult, administer oxygen. ・If cardiac arrest occurs (unresponsive and not breathing normally), begin chest compressions and rescue breathing; use an AED if available. | 
 | If on skin | ・Remove all contaminated clothing at once. ・Rinse the affected skin thoroughly with running water or shower, then wash with soap and water. ・Lay the victim in a quiet, warm place to prevent hypothermia. ・Seek medical attention. ・Be aware of simultaneous vapor exposure. | 
 | If in eyes | Hold the eyelids open and flush the eyes with running water for at least 10 minutes. | 
 | If swallowed | ・Rinse the mouth and have the victim spit out any liquid. ・Do not induce vomiting. ・Note that toxic effects may be delayed. ・If spontaneous vomiting occurs, to prevent aspiration, lower the head below the chest and place the victim face-down in the prone position. | 

## Slide 97: Class II Specified Chemical Substances
p-Dimethylaminoazobenzene (CH₃)₂N–C₆H₄–N=N–C₆H₅ CAS RN:60-11-7 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Airway disorders, Urinary tract disorders, Urinary tract tumors, Liver disorders, Suspected carcinogenicity(liver cancer) | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Cough, Sore throat,, Wheezing, Respiratory irritation, Itching, Skin redness, Hematuria, Frequent urination, Painful urination, Lower abdominal pain, Sensation of incomplete bladder emptying, General fatigue, Weight loss | 
Handling Precautions | ・Avoid inhaling dusts or vapors. ・Do not eat, drink or smoke in work areas. ・Keep containers tightly closed. ・Wash hands thoroughly after handling. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Organic-gas respirator with dust-filter function (Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | Move to fresh air and rest in a comfortable position. | 
 | If on skin | ・Wash the area with plenty of water and soap. ・If irritation occurs, consult a physician. | 
 | If in eyes | Rinse eyes under running water for several minutes, holding eyelids open. Seek medical attention. | 
 | If swallowed | Give 1–2 cups of water to drink. | 

## Slide 98: Class II Specified Chemical Substances
p-Nitrochlorobenzene Cl–C₆H₄–NO₂ CAS RN:100-00-5 |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders, Hematologic disorders(hemolytic anemia, methemoglobinemia), Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, facial pallor, Palpitations(tachycardia), Unsteadiness, Cyanosis, Urine discoloration, Weight loss | 
Handling Precautions | ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in work areas. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Organic-gas-type respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Seek medical examination and treatment immediately. ・Notify a physician. | 
 | If on skin | ・Wash affected skin with plenty of water and soap. ・Special medical treatment may be required. ・Remove all contaminated clothing at once and launder before reuse. | 
 | If in eyes | Rinse eyes with plenty of water for several minutes, removing contact lenses if easy to do. Seek medical care. | 
 | If swallowed | ・If feeling unwell, seek medical attention. ・Rinse mouth. | 

## Slide 99: Class II Specified Chemical Substances
Arsenic and its compounds As CAS RN:7440-38-2,1327-53-3,7784-46-5,637-03-6,12279-90-2,etc. |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders(e.g. hyperpigmentation, keratosis), Peripheral neuropathy(e.g. neuritis of the lower limbs), Airway disorders, Lung cancer, Skin cancer, Nasal septum perforation, Liver disorders, Kidney disorders, Digestive system disorders, Hematologic disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Skin inflammation, Itching, Skin redness, Sensory and motor disturbances of the limbs, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Stomatitis, Constipation, Skin hyperpigmentation, depigmentation, keratinization, Ulcers, atrophy or loss of nails and hair, General fatigue, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Abdominal pain, Diarrhea, Vomiting, Loss of appetite, Facial pallor, Palpitations, Dizziness, Unsteadiness, Weight loss | 
Handling Precautions (Arsenic) | ・Keep away from heat, sparks, open flame and other ignition sources. ・Store in a cool place. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in work areas. ・Avoid inhaling dusts or vapors. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex 〇, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Arsenic) | If inhaled | ・Call a physician immediately. ・Move the victim to fresh air and have them rest in a comfortable breathing position. ・If symptoms such as breathing difficulty appear, seek medical attention. ・Have the victim rinse their mouth and spit out any fluid. ・If unconscious but breathing, place on their side in a stable position and protect against hypothermia. ・If breathing is difficult, administer oxygen. ・If airway irritation occurs, administer inhaled glucocorticoid spray as soon as possible. | 
 | If on skin | ・Remove all contaminated clothing at once. ・Protect yourself and move the victim away from the hazard. ・Rinse the affected area under running water or shower for several minutes, then wash thoroughly with water and soap. | 
 | If in eyes | ・Hold the eyelids open and rinse with running water for at least 10 minutes. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・If conscious, induce vomiting. ・ If vomiting occurs spontaneously, to prevent aspiration position the head lower than the chest and place the victim face-down. | 

## Slide 100: Class II Specified Chemical Substances
Hydrogen fluoride HF CAS RN:7664-39-3 |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Anterior eye disorders, Airway disorders, Pulmonary disorders, Cardiovascular disorders, Dental disorders, Bone abnormalities | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Cough, Shortness of breath, Runny, Stuffy nose, Nasal/throat pain, Chest pain, Respiratory distress, General fatigue, Weight loss, Oral pain, Toothache, Tooth discoloration | 
Handling Precautions | ・Avoid inhaling dusts or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in work areas. ・Use only outdoors or in well-ventilated areas. ・Prevent release to the environment. ・If ventilation is insufficient, wear respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Hydrogen fluoride–rated gas respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and help them rest in a comfortable breathing position. ・Call a physician immediately. ・If feeling unwell, seek medical attention. ・Urgent specialized treatment is often required. | 
 | If on skin | ・Remove all contaminated clothing at once. ・Rinse affected skin thoroughly with water (or shower). ・Call a physician immediately. ・special treatment is required. ・ If available, apply calcium gluconate gel to affected areas. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Rinse eyes under running water for several minutes, holding eyelids open. Remove contact lenses if easy to do, then continue rinsing. ・Call a physician immediately. | 
 | If swallowed | ・Rinse mouth. ・Give 1–2 cups of water or milk to drink. ・Do not induce vomiting. | 

## Slide 101: Class II Specified Chemical Substances
β－Propiolactone O═CH₂–CH₂–C(=O)–O CAS RN:57-57-8 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Airway disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Cough, Sputum, Shortness of breath, Chest pain, Respiratory distress, Nasal/throat pain, General fatigue, weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flame and other ignition sources. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in work areas. ・Avoid inhaling dust or vapors. ・Use only outdoors or in well-ventilated areas. ・If ventilation is inadequate, wear respiratory protection. ・Keep containers tightly closed. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Organic-gas respirator (Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and have them rest in a comfortable position. ・Artificial respiration may be required. ・Seek medical attention immediately. | 
 | If on skin | Rinse the affected area under running water or shower for at least 10–20 minutes. | 
 | If in eyes | Rinse eyes with plenty of water for several minutes, removing contact lenses if easy to do. Continue flushing and seek medical care. | 
 | If swallowed | ・Rinse mouth, have the victim spit out the liquid. Give 1–2 cups of water to drink. ・Do not induce vomiting. ・Seek medical attention immediately. | 

## Slide 102: Class II Specified Chemical Substances
Benzene C6H6 CAS RN:71-43-2,1076-43-3,etc. |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Peripheral neuropathy, Respiratory(airway)disorders, Cardiovascular disorders, Immune system disorders, Hematopoietic disorders(e.g. aplastic anemia), Suspected reproductive toxicity, Suspected carcinogenicity(leukemia) | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Pruritus, Erythema, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory disturbances and motor impairment of the extremities, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Facial pallor, Palpitations, Syncope, Altered consciousness, Bleeding tendency(nosebleeds, subcutaneous hemorrhage, bruising), Unsteadiness, Weight loss | 
Handling Precautions | ・Keep away from heat, high temperatures, sparks, open flames and other ignition sources ・Keep containers tightly closed ・Take measures to prevent static‐electric discharge ・Use only outdoors or in well-ventilated areas ・Wash hands thoroughly after handling ・Do not inhale dust or vapor ・Do not eat, drink or smoke in the work area ・Prevent release to the environment |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Organic-gas-type respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move to fresh air; allow to breathe normally or administer oxygen ・If breathing stops, perform artificial respiration ・Seek medical attention immediately | 
 | If on skin | ・Remove contaminated clothing ・Wash affected area thoroughly with water and soap. ・Seek medical attention. | 
 | If in eyes | ・Rinse with plenty of water for at least 10 minutes. ・Remove contact lenses if easily removable and continue rinsing. ・Seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・Do not induce vomiting. ・Seek medical attention. | 

## Slide 103: Class II Specified Chemical Substances
Pentachlorophenol and its sodium salts C₆Cl₅OH CAS RN:87-86-5,131-52-2,etc. |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory disorders, Liver disorders, Kidney disorders, Cardiovascular disorders, Gastrointestinal disorders, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Chloracne, Hyperpigmentation, Follicular keratosis, Nail discoloration, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, Loss of appetite, Sweet‐food craving, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Easy fatigability, Jaundice, Hematuria, Polyuria, Oliguria, Edema, Abdominal pain, Diarrhea, Palpitations, Weight loss | 
Handling Precautions (Pentachlorophenol) | ・Keep containers tightly closed. ・Do not inhale dust or vapors. ・Avoid contact with eyes, skin, and clothing. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in well-ventilated areas. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ×, Chloroprene 〇, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor or dust concentrations, such as ‘third control zones,’ or locations where vapors or dust are released due to leakage.
 | Type of respiratory protection |  | Organic‐gas respirator with dust filter(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Pentachlorophenol) | If inhaled | ・Move the victim to fresh air and let them rest in a position comfortable for breathing. ・Contact a physician immediately. ・Place in a semi-recumbent (half-sitting) position. ・Give artificial respiration if breathing is inadequate. | 
 | If on skin | ・Wash thoroughly with plenty of water and soap. ・Contact a physician immediately. ・If skin irritation develops, seek medical attention. | 
 | If in eyes | ・Rinse carefully with water for several minutes. Remove contact lenses if easily removable, then continue rinsing. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Contact a physician immediately. ・Rinse mouth. ・Administer activated charcoal suspended in water. ・Give one to two glasses of water. | 

## Slide 104: Class II Specified Chemical Substances
Formaldehyde HCHO CAS RN:50-00-0,30525-89-4,etc. |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Skin sensitization, Central nervous system disorders, Airway/lung disorders, Respiratory sensitization, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Erythema, Eczema, Urticaria, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny nose, Nasal congestion, Nasal/throat pain, Chest pain, Respiratory distress, Asthma‐like attacks, Weight loss | 
Handling Precautions | ・Keep away from heat, high temperatures, sparks, open flames and other ignition sources ・Wash hands thoroughly after handling ・Do not eat, drink or smoke in the work area ・Do not inhale dust or vapor ・Use only outdoors or in well‐ventilated areas ・If ventilation is inadequate, wear appropriate respiratory protection ・Do not remove contaminated work clothing from the work area ・Prevent release to the environment |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Formaldehyde‐rated gas mask or equivalent(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move victim to fresh air; place in semi-recumbent (half-sitting) position ・If breathing is difficult, administer oxygen; consider repeated deep inhalations of a glucocorticoid spray. ・Seek immediate medical attention | 
 | If on skin | ・Remove contaminated clothing ・Rinse skin under running water for 10–20 minutes. ・Seek medical attention. | 
 | If in eyes | ・Rinse eyes with plenty of water for at least 10 minutes. ・Seek immediate medical attention. | 
 | If swallowed | ・Rinse mouth. ・If conscious, give ~200 mL (1 glass) of water; if available, 1–2% ammonium chloride, ammonium carbonate, or 20% urea solution. ・Seek medical attention. | 

## Slide 105: Class II Specified Chemical Substances
Magenta NH₂–C₆H₄–C⁺(=NH)–C₆H₃(CH₃)–C₆H₄–NH₂ · Cl⁻ CAS RN:632-99-5 |  |  | 
Health Hazards | Possible Diseases | Urinary system disorders, Urinary tract tumors | 
 | Symptoms | Hematuria(blood in urine), Frequent urination, Dysuria(painful urination), Lower abdominal pain, Sensation of incomplete bladder emptying, General fatigue, Weight loss | 
Handling Precautions | ・Do not inhale dust or vapor. ・Do not eat, drink, or smoke in the work area. ・Keep containers tightly closed. ・Wash hands thoroughly after handling. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | If feeling unwell, seek medical attention. | 
 | If on skin | ・Wash affected area with water and soap. ・If skin irritation occurs, seek medical attention. | 
 | If in eyes | ・Rinse carefully with water for several minutes. ・If eye irritation persists, seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, seek medical attention. | 

## Slide 106: Class II Specified Chemical Substances
Manganese and its compounds Mn CAS RN:7439-96-5,7722-64-7,1313-13-9,13446-34-9,15244-36-7,etc. |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders(speech impairment, gait disturbance, tremor, etc.), Respiratory tract disorders, Lung disorders, Suspected reproductive toxicity | 
 | Symptoms | Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Rhinorrhea, Nasal congestion, Nasal/throat pain, Mask-like facies, Pasty complexion, Drooling, Abnormal sweating, Hand tremor, Poor handwriting, Gait disturbance, Involuntary movements, Speech abnormalities(Parkinson-like syndrome), Chest pain, Respiratory distress | 
Handling Precautions (Manganese) | ・Do not inhale dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Manganese) | If inhaled | ・Move victim to fresh air. ・If breathing difficulty occurs, administer oxygen. ・Seek medical attention immediately. | 
 | If on skin | Wash affected area thoroughly with soap and water. | 
 | If in eyes | ・Rinse eyes with running water for at least 10 minutes. ・Seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・Give a glass of water. ・Do not induce vomiting. ・Seek medical attention. | 

## Slide 107: Class II Specified Chemical Substances
Methyl iodide CH3I CAS RN:74-88-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Respiratory tract disorders, Central nervous system disorders(e.g. visual impairment, speech impairment, ataxia), Mental disorders(delirium, mania), Endocrine disorders(thyroid) | 
 | Symptoms | Eye pain, Tearing, Conjunctival hyperemia, Dermatitis, Itching, Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Delirium, Mania, Vomiting, General fatigue, Cough, Shortness of breath, Runny or stuffy nose, Nasal/throat pain | 
Handling Precautions | ・Do not inhale dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in a well-ventilated area. ・If ventilation is inadequate, wear appropriate respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Methyl-iodide rated gas mask or equivalent(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・If the person feels unwell, seek medical attention. ・Move to fresh air and rest in a comfortable breathing position. ・Contact a physician immediately. | 
 | If on skin | ・Wash thoroughly with plenty of water and soap. ・If irritation or malaise occurs, seek medical attention. ・Remove contaminated clothing and launder before re-use. ・If feeling unwell, seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. ・Contact a physician immediately. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, seek medical attention. | 

## Slide 108: Class II Specified Chemical Substances
Welding fumes Chemical formula：not specified CAS RN: not specified |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders, Airway disorders, Lung disorders, Suspected carcinogenicity | 
 | Symptoms | Parkinson‐like syndrome(Mask-like facies/drooling/abnormal sweating/finger tremor/poor handwriting/gait disturbance/involuntary movements/speech abnormalities), Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Motor neuron impairment, Cough, Shortness of breath, Runny or blocked nose, Nasal/throat pain, Chest pain, Respiratory distress, Weight loss | 
Handling Precautions (Welding fumes：Mn5%,Si10%, Ti10%,Mg5%) | ・Wear appropriate PPE: safety goggles or welding face shield, respiratory protection, safety shoes, flame-resistant work clothing, gloves. ・Do not eat, drink or smoke in the work area. ・Wash hands thoroughly after handling. ・Use only outdoors or in a well-ventilated area. |  | 
Required Protective Equipment | ・Flame-resistant work clothing (protects against heat and sparks) Protective gloves and safety footwear ・Welding face shield or UV-filtering goggles ・Respiratory protection suitable for welding fume particulates |  | 
 | Areas Requiring Respiratory Protection |  | Any location where welding fumes are generated
 | Type of respiratory protection |  | particulate respirator (must meet the Assigned Protection Factor determined by individual exposure measurements; consult the manufacturer)
First Aid Measure (Welding fumes：Mn5%,Si10%, Ti10%,Mg5%) | If inhaled | ・Move the person to fresh air and have them rest in a comfortable position for breathing. ・If they feel unwell or develop respiratory symptoms, seek medical attention | 
 | If on skin | ・Wash the affected area with plenty of water and soap ・If feeling unwell, seek medical attention. ・Launder contaminated clothing before reuse. ・If irritation or rash appears, seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes, removing contact lenses if easy to do, then continue rinsing. ・If irritation persists, seek medical attention. | 
 | If swallowed | ・Seek medical attention immediately. ・Rinse mouth. | 

## Slide 109: Class II Specified Chemical Substances
Refractory ceramic fibers Amorphous man-made mineral fibers primarily composed of Al₂O₃ and SiO₂ CAS RN:142844-00-6 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Respiratory tract disorders, Lung disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Cough, Shortness of breath, Runny or blocked nose, Nasal/throat pain, Chest pain, Difficulty breathing, General fatigue, Weight loss | 
Handling Precautions | ・Wash hands thoroughly after handling. ・Use only outdoors or in a well-ventilated area. ・Avoid inhaling dust or fibers. ・Do not eat, drink, or smoke in the work area. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Tasks involving insulation or refractory work on furnaces/kilns Repair, demolition, or crushing operations Operations where fiber concentration ≥ 0.3 fibers/cm³ by measurement Any unmeasured tasks with potential for high exposure
 | Type of respiratory protection |  | Powered air-purifying respirator (PAPR) or equivalent(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | Move the person to fresh air and keep them in a position that eases breathing. | 
 | If on skin | Rinse the affected area under running water or in a shower, then wash thoroughly with soap and water. | 
 | If in eyes | Hold the eyelids open and rinse eye with running water for at least 10 minutes. | 
 | If swallowed | Rinse mouth and spit out any liquid. | 

## Slide 110: Class II Specified Chemical Substances
Sulfur hydride H2S CAS RN:7783-06-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders, Lung disorders, Cardiovascular disorders, Gastrointestinal disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness/corneal abnormalities, Dermatitis, itching, skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Insomnia, Easy fatigability, Irritability, Abdominal pain, Diarrhea, Nausea, Appetite loss, Dental changes(e.g. tooth discoloration), Cough, Shortness of breath, Runny/stuffy nose, Nasal/throat pain, Chest pain, Breathing difficulty | 
Handling Precautions | ・Keep away from heat, sparks, open flame and hot surfaces. ・Avoid inhaling dust, mist or vapor. ・Use only outdoors or in a well‐ventilated area. ・If ventilation is inadequate, wear appropriate respiratory protection. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene: no data, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Acid‐gas respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move victim to fresh air; keep in a position that eases breathing. ・Seek medical attention immediately. | 
 | If on skin | ・Wash affected area with water. ・If unwell, seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes.水Remove contact lenses if easily done and continue rinsing. ・If irritation persists, obtain medical care. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, seek medical attention. | 

## Slide 111: Class II Specified Chemical Substances
Dimethyl sulfate (CH₃)₂SO₄ CAS RN:77-78-1 |  |  | 
Health Hazards | Possible Diseases | Skin damage, Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders, Lung disorders, Liver damage, Kidney damage, Cardiovascular disorders, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Easy fatigability, Jaundice, Cough, Shortness of breath, Runny or stuffy nose, Nasal/throat pain, Chest pain, Respiratory distress, Hematuria, Polyuria, Oliguria, Edema, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flame and hot surfaces. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Do not inhale dust or vapor. ・Use only outdoors or in a well-ventilated area. ・If ventilation is inadequate, wear appropriate respiratory protection. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene 〇, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Organic-gas-type respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・Emergency medical treatment is necessary. ・Call a physician immediately. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Wash skin thoroughly with running water or shower. ・Call a physician at once. ・Wash contaminated clothing before reuse. ・Specialized medical treatment may be required. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easy to do, then continue rinsing. ・Call a physician immediately. ・Specialized medical treatment may be required. | 
 | If swallowed | ・Rinse mouth; do not induce vomiting. ・Call a physician immediately. ・Specialized medical treatment may be required. | 

## Slide 112: Class III Specified Chemical Substances
Ammonia NH3 CAS RN:7664-41-7 |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Anterior eye disorders, Central nervous system disorders, Airway disorders, Lung disorders, Respiratory sensitization | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Dyspnea, Asthma-like attacks, Runny or stuffy nose, Nasal/throat pain, Chest pain, Respiratory distress | 
Handling Precautions | ・Keep away from heat, sparks, open flames and other ignition sources. ・Use only outdoors or in a well-ventilated area. ・Do not inhale dust or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene △, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Ammonia-rated gas mask or cartridge respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・If the victim is unconscious but breathing, place them in the recovery position on their side and protect against hypothermia. ・At first signs of airway irritation, administer inhaled glucocorticoid spray (if available) to relieve bronchospasm. ・If breathing is difficult, provide oxygen. ・Help the victim assume a semi-sitting position if possible. ・Rescuers must protect themselves throughout. ・In case of cardiac arrest, begin chest compressions and rescue breathing immediately; use an AED if available. ・Call a physician and move the victim to fresh air; keep them at rest in a comfortable breathing position. ・Seek medical attention for any respiratory or other symptoms. | 
 | If on skin | ・Protect yourself while removing the victim from the source of danger. ・Do not peel off garments frozen to the skin; wait until thawed naturally. ・Rinse affected skin under running water or shower for at least 20 minutes. ・Call a physician. | 
 | If in eyes | ・Hold the uninjured eye closed or shielded; rinse the injured eye under running water for at least 10 minutes, keeping lids open. ・Seek immediate medical attention if irritation persists. | 
 | If swallowed | ・Rinse mouth; do not induce vomiting. ・If conscious, give 1–2 cups of water to drink. | 

## Slide 113: Class III Specified Chemical Substances
Carbon oxide CO CAS RN:630-08-0 |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders(ataxia, visual disturbance, color-vision defects, vestibular dysfunction, etc.), Mental disorders(hallucinations, delirium), Blood system disorders, Cardiovascular disorders, Suspected reproductive toxicity | 
 | Symptoms | Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Memory impairment, Hallucinations, Delirium, Facial pallor, Tachycardia(palpitations), Unsteadiness | 
Handling Precautions | ・Keep away from heat, sparks, open flames and hot surfaces. ・Use only outdoors or in a well-ventilated area. ・Do not inhale dust or vapor. ・After handling, wash hands thoroughly. ・No eating, drinking or smoking in the work area. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Locations where CO may leak or accumulate (high-exposure risk areas)
 | Type of respiratory protection |  | Carbon monoxide gas mask or air-purifying respirator with a CO cartridge (Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and keep them resting in a position that eases breathing. ・Seek medical attention immediately. | 
 | If on skin | ・Wash affected area thoroughly with soap and water. ・Obtain medical care if irritation or symptoms develop. | 
 | If in eyes | ・Rinse cautiously with running water for several minutes. ・Seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・Seek medical attention. | 

## Slide 114: Class III Specified Chemical Substances
Hydrogen chloride HCl CAS RN:7647-01-0 |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Anterior eye disorders, Respiratory tract disorders, Lung disorders, Respiratory sensitization, Dental disorders(tooth erosion) | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Cough, Shortness of breath, Asthma-like attacks, Runny or stuffy nose, Nasal/throat pain, Chest pain, Breathing difficulty, Oral pain, Toothache | 
Handling Precautions | ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated area. ・Avoid inhaling dust, mist or vapor. ・If ventilation is inadequate, wear appropriate respiratory protection. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene △, Neoprene 〇 (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Acid‐gas respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・If the victim is unconscious but breathing, place them in a stable recovery position on their side and protect from hypothermia. ・At first signs of airway or respiratory irritation, administer an inhaled glucocorticoid spray if available. ・If breathing is difficult, provide supplemental oxygen. ・In case of cardiac arrest, begin chest compressions and rescue breathing immediately; use an AED if available. ・Note that symptoms may be delayed—monitor closely. ・Call a physician and move the victim to fresh air; keep them resting in a comfortable breathing position. half-sitting position ・If breathing stops, perform artificial respiration. Mouth-to-mouth resuscitation should only be performed in emergency situations. ・If feeing unwell or experience symptoms related to breathing, seek medical attention. | 
 | If on skin | ・Wear protective gloves when administering first aid。 ・Protect yourself while removing the victim from the source of danger. ・Rinse the affected area under running water or shower for at least 20 minutes. | 
 | If in eyes | ・While protecting the uninjured eye, rinse the injured eye under running water for at least 10 minutes, holding the eyelids open. ・Rinse the eyes carefully under running cold water only. Do not leave contact lenses in place. ・If irritation persists, obtain medical care. | 
 | If swallowed | ・Rinse the mouth. Do not give anything to the mouth of an unconscious person. ・Contact a doctor immediately. ・Do not induce vomiting unless directed by a doctor. | 

## Slide 115: Class III Specified Chemical Substances
Nitric acid HNO3 CAS RN:7697-37-2 |  |  | 
Health Hazards | Possible Diseases | Skin damage, Anterior eye disorders, Upper airway disorders, Lung disorders, Dental erosion | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Cough, Shortness of breath, Runny or stuffy nose, Nasal/throat pain, Chest pain, Difficulty breathing, Oral pain, Toothache | 
Handling Precautions | ・Keep away from heat, sparks, open flame and hot surfaces. ・Keep away from clothing and other combustible materials. ・Prevent mixing with combustible substances. ・Do not transfer to other containers. ・Avoid inhaling dust, mist or vapor. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated area. ・If ventilation is inadequate, wear appropriate respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Acid‐gas respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and keep them resting in a comfortable breathing position. ・Contact a physician immediately. ・If feeling unwell, seek medical attention. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Contact a physician immediately. ・Flush the affected area with water or shower thoroughly. ・If feeling unwell, seek medical attention. ・Wash contaminated clothing before reuse. | 
 | If in eyes | ・Contact a physician immediately. ・Rinse cautiously under running water for several minutes. Remove contact lenses if easily done, then continue rinsing. ・If irritation or discomfort persists, seek medical attention | 
 | If swallowed | ・Contact a physician immediately ・Rinse mouth; do not induce vomiting ・If feeling unwell, seek medical attention. | 

## Slide 116: Class III Specified Chemical Substances
Sulphur dioxide SO2 CAS RN:7446-09-5 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Respiratory tract disorders, Lung disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Cough, Shortness of breath, Runny or stuffy nose, Nasal/throat pain, Chest pain, Difficulty breathing | 
Handling Precautions | ・Wear chemical‐splash goggles or a face shield ・Avoid inhaling the gas ・Use only outdoors or in a well-ventilated area ・No eating, drinking or smoking in the work zone ・Wash hands thoroughly after handling |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ○, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Acid‐gas respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and keep them resting in a comfortable breathing position. ・Seek medical attention. ・If feeling unwell, seek medical attention. | 
 | If on skin | ・Rinse affected area immediately. ・Seek medical attention. ・If feeling unwell, seek medical attention. | 
 | If in eyes | ・Rinse cautiously under running water for several minutes. Remove contact lenses if easily done, then continue rinsing. ・If irritation persists, obtain medical care. ・Seek medical attention. ・If feeling unwell, seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・Seek medical attention. ・If feeling unwell, seek medical attention. | 

## Slide 117: Class III Specified Chemical Substances
Phenol C₆H₅OH CAS RN:108-95-2 |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders, Lung disorders, Liver disorders, Kidney disorders, Blood‐system disorders, Cardiovascular disorders, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Easy fatigability, Jaundice, Cough, Shortness of breath, Runny or stuffy nose, Nasal/throat pain, Chest pain, Difficulty breathing, Hematuria, Polyuria, Oliguria, Edema,, Facial pallor, Tachycardia(Palpitations), Unsteadiness | 
Handling Precautions | ・Do not eat, drink or smoke in the work area. • Use appropriate personal protective equipment and ensure adequate ventilation to minimize exposure. • Avoid inhaling dust. • Wash hands thoroughly after handling. • Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene 〇, Neoprene 〇 (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Organic-gas-type respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move victim to fresh air and have them rest in a position that eases breathing. ・Call a physician immediately. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Gently wash affected area with plenty of soap and water. ・Seek medical attention. ・Wash contaminated clothing thoroughly before reuse. | 
 | If in eyes | ・Remove contact lenses if easily done and continue rinsing. ・Rinse cautiously with water for several minutes. ・Call a physician immediately. | 
 | If swallowed | ・Rinse mouth. Call a physician immediately. ・Do not induce vomiting. | 

## Slide 118: Class III Specified Chemical Substances
Phosgene COCl2 CAS RN:75-44-5 |  |  | 
Health Hazards | Possible Diseases | Skin disorders, Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders, Lung disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Erythema, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny or stuffy nose, Nasal/throat pain | 
Handling Precautions | ・Keep the container tightly closed. ・Avoid inhaling dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated space. ・Wear appropriate respiratory protection. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Halogen-gas cartridge respirator or equivalent(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the person to fresh air and have them rest in a semi-sitting posture. ・Administer oxygen if breathing is difficult. ・Call a physician immediately. | 
 | If on skin | ・Rinse the affected area with large amounts of water and soap. ・In case of frostbite (freezing), flush with plenty of water but do not remove clothing immediately. ・Seek medical evaluation and treatment if irritation develops. | 
 | If in eyes | ・Rinse cautiously under running water for several minutes. Remove contact lenses if easily done, then continue rinsing. ・Seek medical attention if eye irritation persists. | 
 | If swallowed | ・Rinse mouth. ・Seek medical attention if discomfort or symptoms occur. | 

## Slide 119: Class III Specified Chemical Substances
Sulfuric acid H2SO4 CAS RN:7664-93-9,8014-95-7 |  |  | 
Health Hazards | Possible Diseases | Skin damage, Anterior eye disorders, Upper airway disorders, Lung disorders, Dental erosion | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Skin redness, Cough, Shortness of breath, Runny or stuffy nose, Nasal/throat pain, Chest pain, Difficulty breathing, Oral pain, Toothache | 
Handling Precautions | ・Do not transfer to other containers. • Avoid inhaling dust, mist or vapor. • Use only outdoors or in a well-ventilated area. • If ventilation is inadequate, wear appropriate respiratory protection. • Wash hands thoroughly after handling. • No eating, drinking or smoking in the work area. • Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex 〇, Chloroprene △, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Locations where acid mist may leak or accumulate (high-exposure risk areas)
 | Type of respiratory protection |  | Dust/acid-gas combination respirator or cartridge for acidic gases(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move victim to fresh air. ・If breathing is difficult, have them sit up and administer oxygen; consider repeated deep inhalations of glucocorticoid spray. ・If breathing stops, perform artificial respiration. ・Obtain medical attention immediately | 
 | If on skin | ・Remove contaminated clothing. ・Flush affected area with water for at least 10 minutes. Because concentrated acid reacts exothermically, you may first blot with a dry cloth or tissue, then rinse thoroughly with copious water or shower. ・Seek medical attention. | 
 | If in eyes | ・Rinse under running water for at least 10 minutes, holding eyelids open; remove contact lenses if easily done and continue irrigation ・To remove residual acid, use a gentle jet of water directed into the eye and continue flushing even during transport ・Seek medical attention. | 
 | If swallowed | ・Rinse mouth. ・Have the person drink a glass of water (do not neutralize with base or give activated charcoal). ・Do not induce vomiting. ・Seek medical attention immediately. | 

## Slide 120: Specified Chemical Substances
1,3-Butadiene CH₂=CH–CH=CH₂ CAS RN:106-99-0 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Central nervous system disorders, Respiratory tract disorders, Liver disorders, Cardiovascular system disorders, Blood‐system disorders, Female reproductive toxicity, Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Cough, Shortness of breath, Runny or stuffy nose, Nasal/throat pain, Easy fatigability, Jaundice, Facial pallor, Palpitations, Unsteadiness, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flame or other ignition sources. ・Avoid inhaling dust or vapors. ・Wash hands thoroughly after handling. ・No eating, drinking or smoking in the work area. ・Use only outdoors or in a well-ventilated area. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Organic-gas-type respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the victim to fresh air and have them rest in a position comfortable for breathing. ・Seek medical attention. | 
 | If on skin | ・In case of frostbite, flush the affected area with large amounts of water; do not remove frozen clothing. ・Seek medical attention. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easily done and continue rinsing. ・If irritation persists, obtain medical evaluation and treatment. | 
 | If swallowed | Rinse mouth with water. Seek medical evaluation and treatment. | 

## Slide 121: Specified Chemical Substances
1,4-Dichloro-2-butene ClCH₂–CH=CH–CH₂Cl CAS RN:764-41-0 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Central nervous system disorders, Respiratory tract disorders, Systemic toxicity (multi-organ effects not limited to a single organ), Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Erythema, General fatigue, Cough, Shortness of breath, Runny or stuffy nose, Nasal/throat pain, Weight loss | 
Handling Precautions | ・Keep away from heat, sparks, open flames and other ignition sources. ・Keep containers tightly closed. ・Take measures to prevent static‐electric discharge. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Avoid inhaling dust or vapors. ・Use only outdoors or in a well-ventilated place. ・Wear appropriate respiratory protection. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene ×, Neoprene × (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Required where vapor may leak or accumulate (high-exposure risk locations).
 | Type of respiratory protection |  | Organic-gas-type respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Immediately seek medical attention. ・Move the person to fresh air and have them rest in a position that eases breathing. | 
 | If on skin | ・Wash the affected area under running water or shower. ・Seek medical attention immediately. ・Remove all contaminated clothing. ・Wash contaminated clothing thoroughly before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easily done, then continue rinsing. ・Seek medical attention immediately. | 
 | If swallowed | ・Rinse mouth. ・Seek medical attention immediately. | 

## Slide 122: Specified Chemical Substances
Diethyl sulfate C₂H₅O–SO₂–OC₂H₅ CAS RN:64-67-5 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Respiratory tract disorders, Lung disorders, Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Erythema, Cough, Shortness of breath, Runny or stuffy nose, Nasal/throat pain, General fatigue, Weight loss | 
Handling Precautions | ・Wash hands thoroughly after handling. • Do not eat, drink or smoke in the work area. • Avoid inhaling dust or vapors. • Prevent release into the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ×, Latex ×, Chloroprene 〇, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Locations where vapor or mist may be released due to leakage (high-exposure risk areas).
 | Type of respiratory protection |  | Organic–gas cartridge respirator with dust filter(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move victim to fresh air and have them rest in a position comfortable for breathing. ・Seek medical attention immediately. | 
 | If on skin | ・Immediately remove all contaminated clothing. ・Seek medical attention immediately. ・Wash affected area thoroughly with water and soap or rinse in a safety shower. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Seek medical attention immediately. ・Rinse cautiously with water for several minutes. Remove contact lenses if easily done, then continue rinsing. | 
 | If swallowed | ・Seek medical attention immediately. ・Rinse mouth with water. Do not induce vomiting. | 

## Slide 123: Specified Chemical Substances
1,3-Propane sultone –(CH₂)₃–SO₂–O– CAS RN:1120-71-4 |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders, Systemic toxicity (multi‐organ effects possible without a single target organ), Suspected carcinogenicity | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, pruritus(Itching), Erythema, General fatigue, Weight loss | 
Handling Precautions | ・Avoid inhaling dust or vapors. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Use only outdoors or in a well-ventilated location. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex △, Chloroprene 〇, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Organic–gas cartridge respirator with dust filter(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. ・Seek medical attention. | 
 | If on skin | ・Wash the affected area thoroughly with plenty of water and soap. ・If irritation occurs, obtain medical evaluation and treatment. ・Wear protective gloves when giving first aid. ・Remove contaminated clothing. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easily done, then continue rinsing. ・If irritation persists, seek medical evaluation and treatment. | 
 | If swallowed | ・Seek medical attention immediately. ・Rinse mouth. | 

## Slide 124: Lead
Lead Pb CAS RN:7439-92-1 |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders, Peripheral nervous system disorders, Kidney disorders, Blood-system disorders (hematopoietic disorders), Cardiovascular system disorders, Immune system disorders, Digestive system disorders (colic, constipation, etc.), Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory disturbances and motor dysfunction in the extremities, Hematuria, Polyuria, Oliguria, Edema, Facial pallor, Palpitations, Unsteadiness, Abdominal pain, Diarrhea, Loss of appetite, Weight loss | 
Handling Precautions | ・Do not eat, drink or smoke in the work area. ・Use appropriate protective equipment and local exhaust or other ventilation to minimize exposure. ・Avoid inhaling dust. ・Wash hands thoroughly after handling. ・Prevent release into the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Move the person to fresh air and have them rest in a position comfortable for breathing. ・If they feel unwell, seek medical attention. | 
 | If on skin | ・Wash the affected area thoroughly. ・If irritation or other symptoms occur, seek medical attention. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. ・If irritation persists, obtain medical evaluation and treatment. | 
 | If swallowed | Rinse mouth promptly. Seek medical evaluation and treatment right away. | 

## Slide 125: Lead
Lead alloys Pb CAS RN:7439-92-1 |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders, Peripheral nervous system disorders, Kidney disorders, Blood-system disorders(hematopoietic disorders), Cardiovascular system disorders, Immune system disorders, Digestive system disorders(colic, constipation, etc.), Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory abnormalities and motor dysfunction of the limbs, Abdominal pain, Diarrhea, Loss of appetite, Facial pallor, Palpitations, Unsteadiness, Weight loss | 
Handling Precautions （solder： Sn60%,Pb40%, Pentaerythrityl Hydrogenated Rosinate2%） | ・Do not eat, drink, or smoke in the work area. ・Wash hands thoroughly after handling. ・Use only outdoors or in a well-ventilated area. ・Avoid inhalation of dust, fumes, or mists. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). |  | 
 | Areas Requiring Respiratory Protection |  | “Control zone 3” areas or any location where dust or welding fumes may be released Places with a risk of high-concentration exposure
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure （solder： Sn60%,Pb40%, Pentaerythrityl Hydrogenated Rosinate2%） | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・If they feel unwell or develop respiratory symptoms, seek medical attention. | 
 | If on skin | ・Wash the affected area thoroughly with plenty of water and soap. ・If they feel unwell, seek medical attention. ・Launder contaminated clothing before reuse. ・If irritation or other symptoms occur, obtain medical evaluation and treatment. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. Remove contact lenses if easily done; continue rinsing. ・If irritation persists, seek medical evaluation and treatment. | 
 | If swallowed | Seek immediate medical attention. Rinse mouth with water. | 

## Slide 126: Lead
Lead compounds Pb CAS RN:6080-56-4,10099-74-8,10101-63-0,1314-13-2,7758-95-4,1317-36-8,etc. |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders, Peripheral nervous system disorders, Kidney disorders, Blood‐system disorders (hematopoietic disorders), Cardiovascular system disorders, Immune system disorders, Digestive system disorders (colic, constipation, etc.), Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory disturbances and motor dysfunction of the limbs, Abdominal pain, Diarrhea, Loss of appetite, Facial pallor, Palpitations, Unsteadiness, Weight loss | 
Handling Precautions (Lead(II) Acetate Trihydrate) | ・Do not eat, drink, or smoke in the work area. ・Wash hands thoroughly after handling. ・Avoid release into the environment. ・Avoid inhaling dust, fumes, or spray. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】(塩化鉛(Ⅱ)) Nitrile ◎, Latex ◎, Chloroprene ◎, Neoprene ◎ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high dust concentration, such as ‘third control zones,’ or locations where dust is released due to leakage.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (Lead(II) Acetate Trihydrate) | If inhaled | Call a physician immediately. | 
 | If on skin | ・If feeling unwell or if irritation occurs, obtain medical evaluation. ・Wash thoroughly with plenty of water and soap. ・Call a physician immediately. | 
 | If in eyes | ・If irritation persists, seek medical attention. ・Rinse cautiously with water for several minutes. ・Call a physician immediately. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, seek medical attention. ・Call a physician immediately. | 

## Slide 127: Lead
Tetraalkyl lead Pb(CnH2n+1)4 CAS RN:75-74-1,78-00-2,etc. |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders, Peripheral nervous system disorders, Mental disorders(delirium, hallucinations, etc.), Gastrointestinal disorders, Hematological disorders | 
 | Symptoms | Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory disturbances and motor dysfunction of the limbs, Abdominal pain, Diarrhea, Loss of appetite, Facial pallor, Palpitations, Unsteadiness, Delirium, Hallucinations | 
Handling Precautions （Tetramethyllead） | ・Keep away from heat, sparks, open flames and other ignition sources. ・Keep the container tightly closed. ・Take precautions against static discharge. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Avoid inhaling vapors or mists. ・Use only outdoors or in a well-ventilated location. ・Wear appropriate respiratory protection. ・Prevent release to the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves. ※ Select glove material appropriate for the chemical. Replace gloves after permeation time has passed(or immediately if permeation time is unknown). 【Glove permeation data (Ministry of Health, Labour and Welfare)】 Nitrile △, Latex ×, Chloroprene ×, Neoprene △ (◎ >240 min, ○ 60–240 min, △ 10–60 min, × <10 min) |  | 
 | Areas Requiring Respiratory Protection |  | Areas with high vapor concentration such as “third control zones” or locations where vapors are released due to leakage.
 | Type of respiratory protection |  | Organic-gas-type respirator(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure （Tetramethyllead） | If inhaled | ・Move to fresh air and keep at rest in a position comfortable for breathing. ・Seek medical attention immediately. ・If feeling unwell, obtain medical treatment. | 
 | If on skin | ・Wash affected area thoroughly. ・If feeling unwell, seek medical attention. ・Launder contaminated clothing before reuse. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. ・If irritation persists or if feeling unwell, seek medical attention. | 
 | If swallowed | ・Seek medical attention immediately. ・Rinse mouth. ・If feeling unwell, obtain medical treatment. | 

## Slide 128: Asbestos
Asbestos(Chrysotile) H2Mg3O8Si2.H2O CAS RN:1332-21-4,2172-73-5,12001-29-5,12001-28-4,etc. |  |  | 
Health Hazards | Possible Diseases | Airway disorders, Pulmonary disorders, Pneumoconiosis(asbestosis), Lung cancer or mesothelioma, Diffuse pleural thickening with marked respiratory impairment, Benign asbestos pleural effusion | 
 | Symptoms | Cough, Shortness of breath, Chest pain, Dyspnea, General fatigue, Weight loss | 
Handling Precautions | ・Avoid inhalation of dust or fibers. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. |  | 
Required Protective Equipment | Disposable chemical-protective coveralls, Goggle-style chemical splash goggles, Protective gloves (Select specific items based on the work task—consult the PPE manufacturer.) |  | 
 | Areas Requiring Respiratory Protection |  | All locations where asbestos is handled
 | Type of respiratory protection |  | Reusable dust respirator with at least an RL2 or RS2 particulate cartridge (Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | Seek medical evaluation and treatment immediately. | 
 | If on skin | ・Wash thoroughly with plenty of water and soap. ・If feeling unwell or if irritation occurs, obtain medical evaluation and treatment. | 
 | If in eyes | ・Rinse cautiously with water for several minutes. ・ If eye irritation persists, seek medical evaluation and treatment. | 
 | If swallowed | ・Rinse mouth. ・If feeling unwell, obtain medical evaluation and treatment. | 

## Slide 129: Dust
Dust(silica) SiO2 CAS RN:7631-86-9,etc, |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders, Peripheral nervous system disorders, Kidney disorders, Blood‐system disorders (hematopoietic disorders), Cardiovascular system disorders, Immune system disorders, Digestive system disorders (colic, constipation, etc.), Suspected carcinogenicity, Suspected reproductive toxicity | 
 | Symptoms | Headache, Head heaviness, Dizziness, Drowsiness, Vomiting, General fatigue, Sensory disturbances and motor dysfunction in the limbs, Abdominal pain, Diarrhea, Loss of appetite, Facial pallor, Palpitations(Tachycardia), Unsteadiness, Weight loss | 
Handling Precautions （silica） | ・Avoid inhaling dust. ・Wash hands thoroughly after handling. ・Do not eat, drink, or smoke in the work area. ・Use only outdoors or in a well-ventilated location. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves.(Select suitable type based on work conditions or consult the manufacturer) |  | 
 | Areas Requiring Respiratory Protection |  | Work zones classified as “third control divisions” or any operations listed in Table 3 of the Dust Hazard Prevention Regulations—i.e. locations with a risk of high dust exposure.
 | Type of respiratory protection |  | Particulate-filtering(dust) mask(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure （silica） | If inhaled | ・Move the person to fresh air. Let them rest in a comfortable, easy-breathing posture. ・If symptoms persist, seek medical attention. | 
 | If on skin | Wash affected area with plenty of water. If irritation or other symptoms continue, consult a physician. | 
 | If in eyes | ・Rinse cautiously with water for 15–20 minutes. Remove contact lenses if easily done, and continue rinsing. ・If irritation persists, seek medical attention. | 
 | If swallowed | Rinse mouth with water. Seek medical evaluation promptly. | 

## Slide 130: Dioxin
Dioxin(TCD) C12H4Cl4O2 CAS RN:1746-01-6(TCD) |  |  | 
Health Hazards | Possible Diseases | Anterior eye disorders, Skin disorders(e.g. chloracne), Liver damage, Kidney damage, Hematologic disorders, Immune system disorders, Urinary system disorders, Endocrine disruption, Carcinogenicity risk, Reproductive toxicity risk, Nervous system disorders | 
 | Symptoms | Eye pain, Tearing, Conjunctival redness, Dermatitis, Itching, Erythema, Chloracne(acneiform eruptions), Headache, Head heaviness, Dizziness, Drowsiness, Nausea, Vomiting, General fatigue, Sensory and motor disturbances of the limbs, Easy fatigability, Jaundice, Hematuria, Frequent urination, Painful urination, Lower abdominal pain, Sensation of incomplete voiding, Dry mouth, Polydipsia, Polyuria, Pallor, Palpitations, Unsteadiness, Weight loss | 
Handling Precautions (TCD) | ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Avoid any contact with eyes, skin or clothing. ・Do not inhale dust or vapors. ・Pregnant or nursing personnel must avoid exposure. ・Use only outdoors or in a well-ventilated area. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves.(Select suitable type based on work conditions or consult the manufacturer) |  | 
 | Areas Requiring Respiratory Protection |  | Any area where dioxin exposure is possible
 | Type of respiratory protection |  | Organic–gas cartridge respirator with dust filter(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure (TCD) | If inhaled | ・Move the victim to fresh air and keep them resting in a position that eases breathing. ・Call a physician immediately. ・If symptoms such as respiratory distress develop, obtain medical examination and treatment. | 
 | If on skin | ・Contact a physician immediately. ・While protecting yourself, remove the victim from the source of contamination. ・Immediately remove all contaminated clothing. ・ Rinse the affected skin thoroughly under running water or shower, then wash gently with soap and water. ・Do NOT use alcohol, gasoline, or any other solvents. | 
 | If in eyes | ・Contact a physician immediately. ・Hold the eyelids wide open and flush the eye with running water for at least 10 minutes. | 
 | If swallowed | ・Contact a physician immediately. ・Rinse mouth and have the victim spit out any liquid. ・If the victim is conscious, give 1–2 glasses of water to drink and induce vomiting. ・Be aware that signs of poisoning may be delayed. | 

## Slide 131: Dioxin
Dioxins(various congeners) C12H8-xClxO2 etc. CAS RN:1746-01-6,51207-31-9,32598-13-3,etc. |  |  | 
Health Hazards | Possible Diseases | Central nervous system disorders,Peripheral nervous system disorders, Skin disorders(e.g. chloracne), Liver damage, Endocrine system disorders, Immune system disorders, Carcinogenicity risk, Reproductive toxicity risk | 
 | Symptoms | Dermatitis, Itching, Skin redness, Acneiform eruptions(chloracne), Headache, Head heaviness, Dizziness, Drowsiness, Nausea, Vomiting, General fatigue, Sensory and motor disturbances of the limbs, Easy fatigability, Jaundice, Dry mouth, Excessive thirst, Polyuria, Unsteadiness, Weight loss | 
Handling Precautions | ・Do not inhale dust or vapors. ・Avoid any contact with eyes, skin or clothing. ・Wash hands thoroughly after handling. ・Do not eat, drink or smoke in the work area. ・Prevent release into the environment. |  | 
Required Protective Equipment | Laboratory coat or work clothing, protective goggles, protective gloves.(Select suitable type based on work conditions or consult the manufacturer) |  | 
 | Areas Requiring Respiratory Protection |  | All areas where dioxin exposure may occur
 | Type of respiratory protection |  | Organic–gas cartridge respirator with dust filter(Select suitable type based on work conditions or consult the manufacturer.)
First Aid Measure | If inhaled | ・Seek medical attention immediately. ・If feeling unwell, obtain professional examination and treatment. | 
 | If on skin | ・Rinse the affected area thoroughly with copious water and soap. ・Remove all contaminated clothing at once; launder before reuse. | 
 | If in eyes | Flush eyes with plenty of water for several minutes (remove contact lenses if easy to do). Seek medical attention. | 
 | If swallowed | ・Seek medical attention immediately; special treatment is required. ・Rinse mouth. ・ Administer water containing suspended activated charcoal; induce vomiting only if the person is fully conscious. |